'****************************************************************************
'* <HybrLo> *
'* My first attempts to writing code for a 16 bit PIC *
'* This is a framework that implements the main features of the chip *
'* as well as the software framework we typically used on 8 bit chips *
'* used for our musical robots: a realtime multitasker *
'* HYBRLO_22_24 *
'* HYBRLO_25_27 *
'* HYBRLO_28_30 *
'* HYBRLO_31_33 *
' ***************************************************************************
' NOTE: Pickit3 must be used for programming these devices!
' Each interrupt has its own handler, simply write one handler for each interrupting
' device without having to work out which interrupt it is.
' Timers are more logical: specify the count going upwards that will trigger an
' interrupt rather than working out when the counter would underflow.
'
'01.08.2016: Test and debug board designed, etched and soldered.
' Programming requires the PiCkit3 programmer. PicKit2 does not work!
'02.08.2016: 1M resistor added over X-tal pins
'03.08.2016: Finaly got the clock up and running on the X-tal
' Working out the MIDI UART now.
' Midi-in buffering implemented.
' Trying to use the pwm channels... we cannot use the HPWM commands...
' Implementing velocity control with timers
' Repeats working now.
'04.08.2016: Adding 12 bit ADC on channel AN0
' Midi out looks like working using the Basic command HSROut
' 1 midi packet (3 bytes) takes some 1ms, which conforms to the standard.
' adding initialisation for the PWM channels
' This is as yet not working...
'05.08.2016: with 60Mhz clock the frequency range for PWM would be 60MHz --> 915Hz
' so, for audio use we need a prescale devider :64
' Thus the frequency range would become 14Hz --> 937.5kHz
'06.08.2016: pwm begint stilaan goed te werken.
' different modes of operation implemented for the pwm channels
' pwmmodus 0 fully debugged.
' pwmmodus 2 fully debugged (3-phase motor control)
' pwmmodus 1 fully debugged (3 independent PWM channels)
' pwmmodus 3 added: AC motor with capacitor phase shifter using 2 pwm channels
' PWM principieel werkend nu.
' eventueel kunnen nog dead times toegevoegd worden indien nodig voor een toepassing
' We kunnen overbodige pwm pinnen nog disablen en beschikbaar maken voor
' andere funkties.
'07.08.2016: Lookup tables for frequencies in 12-tone equal temperament added. Ambitus= 22-127
' looks like it's possible to implement a 3-voice midi synth on this platform.
' Just did it: the 3-channel synth is working!
' Studying the implementation of 32-bit timers
' timers 2/3 and 4/5 implemented as 32-bits timers
' trying to use timer23 instead of our loop counter.
' This now works fine
' We could use timer1 as a motor speed controller for a stepper
' Timer 45 could be used as a high resolution, extreme ambitus tone generator
' Timer 1,4,5 implemented as fast timers in 16 bits for ADSR implementation
' PWM lookups added for this.
'09.08.2016: Further coding. adsr not yet operational. - version saved as 007
'10.08.2016: Different approach to adsr - simplified, using timers
' ADSR works now, but we will need a steep lowpass filter on the output
' with this code we are at the limit of what the PIC can handle.
' As it is now, we can have 6 independent PWM channels.
' For the 3-voice synth we need them all and we used up all available timers.
' The priority settings for the IRQ's are very important for this code to work well.
' This version saved as PIC24_008.bas
'11-12.08.2016: application written for midi-invertor: Mirrored_X.bas. Tested o.k.
' PCB made for this app.
'13.08.2016: metacompiler statements for UART-TX and UART-RX added.
' Buffered midi-out fully implemented.
' For some reason the ADSR pwm is no longer working now...
' Rearranging priority levels made it work again.
' ADSR timers must have a :8 divider setting.
' This version saved as PIC24_009
' There is a lot of jitter on the main loop, so we must be operating close to
' the maximum performance for this chip.
' Working version saved as P14_synth1.bas
'14.08.2016: To relax the interrupt density, we could also invert the pwm functions and
' use the timers 1,4,5 for frequency generation with waveform duty cycle whilst
' the 3 real PWM channel could do the ADRS at the highest possible frequency.
' This requires PWMmodus to be set to 0.
' Coding started.
' looks like PWM needs to be inverted now. Done.
' ADSR works fine now, but the load on the processor is still very high.
' we should try to get the divisions out of the main loop now. Done.\
' Further improvements: decrease nr. of steps for ADSR, as 127 steps
' for an attack time of say 100ms seems largely overkill...
'15.06.2016: ADSR coding restructured to make it more readible.
' Tests o.k. bit we still have glitches and seem to be working at the
' edge of what the processor can do.
' PCB dsign started for an evaluation board for this synth.
'20.08.2016: This design could be used for <HybrLo>
'23.08.2016: Evaluation board finished. This works o.k.
' bug removed in the duty cycle control: cannot be zero!
' Start work on the coding for <HybrLo>
' This file now saved as HybrLo_22_24.bas
'--------------------------------------------------------------------------------------
'23.08.2016: Start delopment of specific HybrLo code.
' This code implements notes 22, 23 and 24 and their octaves.
'29.08.2016: Two boards made with active filters.
' Hub board made as well: this should also filter midi for the note-boards.
' HybrLo channel decided to become 8
'31.08.2016: Recoding for the new controller implementation.
' The PCB's for all notes are ready now.
'01.09.2016: GMT testcode adapted such that we can test this code...
' This firmware copied and renamed as HybrLo_25_27.bas for the second board.
'07.09.2016: Mute logic inverted in the code for all boards.
'11.09.2016: First tests on the assembled robot.
' Mute logic appears to be wrong...
'12.09.2016: Seens working fine now, but we do have intermittent failures.
'13.09.2016: Controller 15 added for global waveshape control.
'20.09.2016: Looks like release is no longer working now...
' We could try to nake the 947 constant for scaling the ADSR smaller
' ADSR_scale constant introduced.
' release bug found: scale multiply forgotten in the noteoff proc.
' if we set ADSR_scale to 1024, we can avoid many multiplies in the code...
' done with the introduction of ADSR_shift = 10
' Program Change command implemented now. Needs further investigations.
' 09.10.2016: All pipes mounted on the instrument...
' Further research into the origins of the glitches.
' PWM freq lowered to 29kHz
' try to give UART lower priority, to avoid glitches
' 10.10.2016: Recoding to avoid float's in the code.
' Now with 40dB scalings.
' Ommited ADSR flags reset on note-On command, was the first cause of the glitches.
' real time modulation of volume added using ctrl's 70-82
' For the other boards, just change the $define Boardx_x compiler metacommand.
' 11.10.2016: Extending range with an octave...
' Programming under high fever conditions...
' extending with yet one more octave...
' Could we add pitch insecurity in a simple way?
' versie 002: 11.10.2016: 40dB dynamiek, maar werkend in de onderste 13 bits
' 12.10.2016: 40dB lookups herberekend voor bovenste bereik van de PWM
' dit zou de S/R verhouding moeten verbeteren.
' 60dB lookups added again.
' This version uploaded. Version 003.
' 13.10.2016: start implementation of ctrl#1 for frequency jitter.
' ADSR periods halved.
' Jitter controller (#1) added
' Release range reset to 512 ms. Attack and decay are now 256ms
' 14.10.2016: Presets modified.

' TO DO:
' implement tuning

''-------------------------------------------------------------------------------------------------------------
' START:
Device = 24EP128MC202
        ' this code should also work on 24EP32MC202, 24EP64MC202, 24EP256MC202, 24EP512MC202
        ' and dsPIC33EP32MC202, dsPIC33EP64MC202, dsPIC33EP128MC202, dsPIC33EP256MC202, dsPIC33EP512MC202
        ' and dsPIC33EP32MC502, dsPIC33EP64MC502, dsPIC33EP128MC502, dsPIC33EP256MC502, dsPIC33EP512MC502
Clear
 ' port-assignments:
 '******************
Symbol poweron_led PORTA.4 ' orange LED
Symbol watchdog_led PORTB.4 ' orange LED
Symbol mute PORTB.5 ' this is pin 14
High mute ' avoiding artefacts on startup

Config FPOR = ALTI2C1_OFF, ALTI2C2_OFF ' unsure about this
Config FWDT = WDTPOST_PS256, WINDIS_OFF, PLLKEN_ON, FWDTEN_OFF ' FWDTEN_OFF disables the WDT (watchdog timer)
RCON.5 = 0 ' clear the watchdog enable bit for reset = SWDTEN_OFF
' first configure the clock...
' select internal FRC at POR not using PLL:
Config FOSCSEL = FNOSC_FRC, IESO_OFF
DelayMS 10
' make sure we assign the correct pins to use for the ICD (Pickit3)
Config FICD = ICS_PGD1, JTAGEN_OFF ' this sets the pins used for the programmer

' enable clock switching and configure POSC for XT mode with 10MHz crystal
Config FOSC = FCKSM_CSECMD, OSCIOFNC_OFF, POSCMD_XT
Main_Setup:
' configure PLL prescaler, PLL postscaler, PLL divisor
PLLFBD = 46
CLKDIV.7 = 0 'PLLPOST N2=2
CLKDIV.6 = 0
CLKDIV.0 = 0 'PLLPRE N1=2
CLKDIV.1 = 0
CLKDIV.2 = 0
CLKDIV.3 = 0
CLKDIV.4 = 0
Write_OSCCONH ($3) ' = __builtin_write_OSCCONH(0x03)
Write_OSCCONL (OSCCON | %1) ' = __builtin_write_OSCCONL(OSCCON | 0x01)
PLL_Setup(48, 2, 2, $0300) ' should set it to 120MHz operation with 10MHz X-tal
        ' Fosc = 10MHz * 48 / 2 * 2 = 120MHz
        ' now we get a 10MHz clock signal on pin OSC2, pin10...
DelayMS 1000 ' wait for stability
Declare Xtal = 120 ' set to Fosc

$define Enable_UART_RX ' midi-in
'$define Enable_UART_TX ' midi-out
'$define Enable_ADC12bit ' precompiler instructions
$define Enable_PWM ' precompiler instructions
$define Enable_Timer1 ' precompiler instructions - 16 bit timer
$define Enable_Timer23 ' 32-bit timer
'$define enable_Timer45 ' 32-bit timer
$define Enable_Timer4 ' as 16 bit timer
$define Enable_Timer5 ' as 16 bit timer

        'Declare Hserial_Baud = 31250 ' USART1 baud rate - set to MIDI
        'Declare Hrsout1_Pin = PORTB.8 ' RP40 ' Select the pin for TX with USART1
        'Declare HRSin1_Pin = PORTB.9 ' RP41
PPS_Output(cOut_Pin_RP40, cOut_Fn_U1TX) ' Map UART1 TX pin to RP40 'RP35
PPS_Input(cIn_Pin_RP41, cIn_Fn_U1RX) ' Map UART1 RX pin to RP41 'RPI34

 'constant initialisations for the midi input parser:
Symbol Midichannel = 8 ' HybrLo_Channel
Symbol NoteOff_Status = 128 + Midichannel ' 2 bytes follow
Symbol NoteOn_Status = 144 + Midichannel
Symbol Keypres_Status = 160 + Midichannel
Symbol Control_Status = 176 + Midichannel
Symbol ProgChange_Status = 192 + Midichannel ' 1 byte message
Symbol Aftertouch_Status = 208 + Midichannel ' 1 byte follows
Symbol Pitchbend_Status = 224 + Midichannel ' lsb msb follow
Symbol NrTasks = 8
'Symbol ADSR_scale = 947 ' this is the timing scale value for all ADSR components
        ' made a symbolic constant 20.09.2016
        ' with this value we had 512ms range for each ADSR step
        ' 12.10.2016: This constant is no longer used in the code
        ' but was replaced with:
Symbol ADSR_shift = 9 ' value << ADSR_shift = value * 1024
        ' 13.10.2016: Changed from 10 to 9
Symbol Release_Shift = 10 ' release back to 512 ms

' change these for other boards:
$define Board22_24
'$define Board25_27
'$define Board28_30
'$define Board31_33

$ifdef Board22_24
Symbol note1 = 22 ' introduced 10.10.2016
Symbol note2 = 23
Symbol note3 = 24
Symbol note1o = note1 + 12 ' 34
Symbol note2o = note2 + 12 ' 35
Symbol note3o = note3 + 12 ' 36
Symbol note1o2 = note1 + 24 ' 46
Symbol note2o2 = note2 + 24 ' 47
Symbol note3o2 = note3 + 24 ' 48
Symbol note1o3 = note1 + 36 ' 58
Symbol note2o3 = note2 + 36 ' 59
Symbol note3o3 = note3 + 36 ' 60
Symbol note1_period = 64355
Symbol note2_period = 60743
Symbol note3_period = 57334
Symbol note1o_period = 32178
Symbol note2o_period = 30372
Symbol note3o_period = 28667
Symbol note1o2_period = 64355 / 4
Symbol note2o2_period = 60743 / 4
Symbol note3o2_period = 57334 / 4
Symbol note1o3_period = 64355 / 8
Symbol note2o3_period = 60743 / 8
Symbol note3o3_period = 57334 / 8

Symbol Att1 = 21 ' controller mapping
Symbol Att2 = 24 ' different for each board.
Symbol Att3 = 27
Symbol Decr1 = 22
Symbol Decr2 = 25
Symbol Decr3 = 28
Symbol Rel1 = 23
Symbol Rel2 = 26
Symbol Rel3 = 29
Symbol Sus1 = 70
Symbol sus2 = 71
Symbol Sus3 = 72
$endif

$ifdef Board25_27
Symbol note1 = 25 ' introduced 10.10.2016
Symbol note2 = 26
Symbol note3 = 27
Symbol note1o = note1 + 12 ' 37
Symbol note2o = note2 + 12 ' 38
Symbol note3o = note3 + 12 ' 39
Symbol note1o2 = note1 + 24 ' 49
Symbol note2o2 = note2 + 24 ' 50
Symbol note3o2 = note3 + 24 ' 51
Symbol note1o3 = note1 + 36 ' 61
Symbol note2o3 = note2 + 36 ' 62
Symbol note3o3 = note3 + 36 ' 63
Symbol note1_period = 54116
Symbol note2_period = 51079
Symbol note3_period = 48212
Symbol note1o_period = 27058
Symbol note2o_period = 25539
Symbol note3o_period = 24106
Symbol note1o2_period = 54116 / 4
Symbol note2o2_period = 51079 / 4
Symbol note3o2_period = 48212 / 4
Symbol note1o3_period = 54116 / 8
Symbol note2o3_period = 51079 / 8
Symbol note3o3_period = 48212 / 8
Symbol Att1 = 31 ' controller mapping
Symbol Att2 = 34
Symbol Att3 = 37
Symbol Decr1 = 32
Symbol Decr2 = 35
Symbol Decr3 = 38
Symbol Rel1 = 33
Symbol Rel2 = 36
Symbol Rel3 = 39
Symbol Sus1 = 73
Symbol sus2 = 74
Symbol Sus3 = 75
$endif

$ifdef Board28_30
Symbol note1 = 28 ' introduced 10.10.2016
Symbol note2 = 29
Symbol note3 = 30
Symbol note1o = note1 + 12 '40
Symbol note2o = note2 + 12 '41
Symbol note3o = note3 + 12 '42
Symbol note1o2 = note1 + 24 '52
Symbol note2o2 = note2 + 24 '53
Symbol note3o2 = note3 + 24 '54
Symbol note1o3 = note1 + 36 '64
Symbol note2o3 = note2 + 36 '65
Symbol note3o3 = note3 + 36 '66
Symbol note1_period = 45506
Symbol note2_period = 42952
Symbol note3_period = 40541
Symbol note1o_period = 22753
Symbol note2o_period = 21476
Symbol note3o_period = 20271
Symbol note1o2_period = 45506 / 4
Symbol note2o2_period = 42952 / 4
Symbol note3o2_period = 40541 / 4
Symbol note1o3_period = 45506 / 8
Symbol note2o3_period = 42952 / 8
Symbol note3o3_period = 40541 / 8
Symbol Att1 = 41 ' controller mapping
Symbol Att2 = 44
Symbol Att3 = 47
Symbol Decr1 = 42
Symbol Decr2 = 45
Symbol Decr3 = 48
Symbol Rel1 = 43
Symbol Rel2 = 46
Symbol Rel3 = 49
Symbol Sus1 = 76
Symbol sus2 = 77
Symbol Sus3 = 78
$endif

$ifdef Board31_33
Symbol note1 = 31 ' introduced 10.10.2016
Symbol note2 = 32
Symbol note3 = 33
Symbol note1o = note1 + 12 '43
Symbol note2o = note2 + 12 '44
Symbol note3o = note3 + 12 '45
Symbol note1o2 = note1 + 24 '55
Symbol note2o2 = note2 + 24 '56
Symbol note3o2 = note3 + 24 '57
Symbol note1o3 = note1 + 36 '67
Symbol note2o3 = note2 + 36 '68
Symbol note3o3 = note3 + 36 '69
Symbol note1_period = 38266
Symbol note2_period = 36118
Symbol note3_period = 34091
Symbol note1o_period = 19133
Symbol note2o_period = 18059
Symbol note3o_period = 17045
Symbol note1o2_period = 38266 / 4
Symbol note2o2_period = 36118 / 4
Symbol note3o2_period = 34091 / 4
Symbol note1o3_period = 38266 / 8
Symbol note2o3_period = 36118 / 8
Symbol note3o3_period = 34091 / 8
Symbol Att1 = 51 ' controller mapping
Symbol Att2 = 54
Symbol Att3 = 57
Symbol Decr1 = 52
Symbol Decr2 = 55
Symbol Decr3 = 58
Symbol Rel1 = 53
Symbol Rel2 = 56
Symbol Rel3 = 59
Symbol Sus1 = 79
Symbol sus2 = 80
Symbol Sus3 = 81
$endif

'constants used for the operation of the PWM modules
' the modus operandi should be set at compile time!
' For the Hybr boards PWMmodus must be 0.
Symbol PWMmodus = 0 ' 0 = all pwm channels have the same period (frequency)
        ' PDC1, PDC2, PDC3 steer the PWM setting for each channel
        ' PTPER is the register to control the period (frequency)
        ' PHASE1, PHASE2, PHASE3 steer the phase between output channels
        ' This mode can be used for ADSR control on 3 channels.
        ' 1 = the three PWM channels have individual period (frequency) controls
        ' controlled with the PHASE1, PHASE2, PHASE3 registers
        ' PDC1, PDC2, PDC3 registers steer the PWM
        ' PWM-value must be < Period
        ' this mode could be used to implement a 3-voice midi synth
        ' We only use the PWMH pins for output here, so portB.15, portB.13 and portB.11
        ' are free and can be used for adrs control
        ' 2 = 3-phase motor control mode
        ' PTPER controls the period (frequency)
        ' MDC controls the duty cycle for the 3 channels
        ' PHASE1, PHASE2, PHASE3 steer the phase between the channels
        ' we start-up with 120 degree phase shifts.
        ' 3 = 2-phase ac motor using a capacitor phase shifter
        ' PTPER controls the period (frequency)
        ' MDC controls the duty cycle for the 3 cha
        ' PHASE1, PHASE2, PHASE3 steer the phase be' port I/O settings:
        ' we start-up with 90 degree phase shifts.

' pwm1H, pwm2H, pwm3H used as ADSR outputs
' we configure the L outputs as normal ports for frequency generator outputs

 TRISA = %100000 ' set to output - we dont use these ports
 TRISB = %0101011100000000
 Output mute
 Output poweron_led
 Output watchdog_led
 High mute ' already done before clock config.
 Low poweron_led

 $ifdef Enable_Timer1
 ' used as tone generator
 IPC0bits_T1IP0 = 1'1 ' set priority - this is very critical!
 IPC0bits_T1IP1 = 0'1 '1 ' set to 5
 IPC0bits_T1IP2 = 1'1 ' 6 = 011
 'TMR1 = 0 ' clear the count
 'PR1 = 65535 ' load Timer1 period
 T1CON.5 = 1 ' set prescaler to :8 = 01 , :64 = 10 , :256 = 11
 T1CON.4 = 0 ' prescaler = 1 = 00 (00 does not work: it freezes the PIC)
 T1CON.15 = 1 ' start
 IFS0bits_T1IF = 0 ' clear Timer1 interrupt flag
 'IEC0bits_T1IE = 1 ' Enable the Timer1 interrupt
 $endif

 $ifdef Enable_Timer23
 T2CONBITs_T32 = 1 ' 32- bit timer start
 T2CONbits_TCS = 0 ' internal clock
 T2CONbits_TON = 1
 T2CONbits_TSIDL = 0
 T2CON.5 = 1 ' pre-scale 256
 T2CON.4 = 1 ' id.
 TMR2 = 0
 TMR3 = 0
 PR2 = 65535
 PR3 = 65535
 IPC2bits_T3IP0 = 1 ' set priority to 1
 IPC2bits_T3IP1 = 0
 IPC2bits_T3IP2 = 0
 IFS0bits_T3IF = 0 ' clear IRQ flag
 IEC0bits_T3IE = 1 ' enable timer 3 interrupt
 $endif

 $ifdef enable_Timer45
 T4CONBITs_T32 = 1 ' 32- bit timer start
 T4CONbits_TCS = 0 ' internal clock
 T4CONbits_TON = 1
 T4CONbits_TSIDL = 0
 T4CON.5 = 1 ' pre-scale 256
 T4CON.4 = 1
 TMR4 = 0
 TMR5 = 0
 PR4 = 65535
 PR5 = 65535
 IPC7bits_T5IP0 = 1 ' set priority to 3
 IPC7bits_T5IP1 = 1
 IPC7bits_T5IP2 = 0
 IFS1bits_T5IF = 0 ' clear IRQ flag
 IEC1bits_T5IE = 1 ' enable timer 5 interrupt
 $endif

 $ifdef Enable_Timer4
 T4CON.15 = 1 ' start timer in 16 bit mode
 T4CON.13 = 0
 T4CON.6 = 0
 T4CON.5 = 1 ' prescaler set to :64
 T4CON.4 = 0 ' 00 = :1, 01 = :8 , 10 = :64, 11 = :256
 T4CON.3 = 0 ' operate as 16 bit timer
 T4CON.1 = 0 ' internal clock
 'TMR4 = 0
 'PR4 = 65535
 IPC6bits_T4IP0 = 1 ' set priority to 5
 IPC6bits_T4IP1 = 0
 IPC6bits_T4IP2 = 1
 Clear IFS1.11 ' clear interrupt flag
 'Set IEC1.11 ' enable interrupt
 $endif

 $ifdef Enable_Timer5
 T5CON.15 = 1 ' start timer in 16 bit mode
 T5CON.13 = 0
 T5CON.6 = 0
 T5CON.5 = 1 ' prescaler set to :64
 T5CON.4 = 0 ' id.
 T5CON.1 = 0 ' internal clock
 'TMR5 = 0
 'PR5 = 65535 ' preset counter
 IPC7bits_T5IP0 = 1 ' set priority to 5
 IPC7bits_T5IP1 = 0
 IPC7bits_T5IP2 = 1
 IFS1bits_T5IF = 0 ' clear IRQ flag
 'IEC1bits_T5IE = 1 ' enable timer 5 interrupt
 $endif

 $ifdef Enable_UART_RX
  ' init UART1-receiver: 31250 Baud
  ' should generate an interrupt for each byte received
 U1MODE.0 = 0 ' = U1MODEbits.STSEL = 0 ' 1 stop-bit
 U1MODE.1 = 0 ' U1MODEbits.PDSEL = 0 ' 8 bit no parity
 U1MODE.2 = 0
 U1MODE.5 = 0 ' =U1MODE_bits.ABAUD = 0 ' no autobauding
 U1MODE.3 = 0 ' = U1MODEbits.BRGH =0 ' 0 = standard speed mode - 16 clocks per bit
 U1MODE.4 = 0 ' logic high is the idle state for the input serial data (default)
 U1MODE.7 = 0 ' wakeup disabled
 U1MODE.8 = 0
 U1MODE.9 = 0
 U1BRG = 119 ' 239 ' voor 120MHz 119 ' voor 60MHz ((60000000 / Hserial_baud) / 16) - 1 ' BRGVAL
 U1STA.5 = 0 ' no bit8
 U1STA.6 = 0 ' U1STAbits.URXISEL = 0 ' receive interrupt mode selection bits
 U1STA.7 = 0 ' interrupt flag is set when a byte is received
 U1MODE.15 = 1 '=U1MODEbits.UARTEN = 1
 U1MODE.12 = 0 ' disable IrDA
 IPC2.12 = 0 ' set priority level to 6 for receiver
 IPC2.13 = 1 ' 1
 IPC2.14 = 1 ' tested with change to 4, 1 step lower then the note timers now...[09.10.2016]
        ' back to 6 on 10.10.2016, as this was not the cause for the glitches.
 IEC0.11 = 1 ' enable IRQ for receiver
 IEC4.1 = 1 ' enable IRQ for error trapping on receiver
 $endif

$ifdef Enable_UART_TX
 U1STA.15 = 0 'interrupt generated when character transferred to tx buffer and buffer is empty
 U1STA.15 = 0
 U1STA.10 = 1 ' transmit enable bit
 U1STA.11 = 0
 Clear IFS0.12 ' clear transmit interrupt flag
 Set IEC0.12 ' enable interrupt
 IPC3.0 = 1
 IPC3.1 = 1
 IPC3.2 = 0 ' set priority to 3
$endif

$ifdef Enable_ADC12bit
 ' init for ADC system: try 12 bit ADC (500kS/s)
 'SMPI1. ADDMAEN = 0
 AD1CON1.15 = 1 ' adc module ON
 AD1CON1.10 = 1 ' select 12-bit mode
 AD1CON1.9 = 0 ' conversion to right alligned integer 0000 dddd dddd dddd
 AD1CON1.8 = 0 ' id.
 AD1CON1.7 = 1 ' auto-convert mode
 AD1CON1.6 = 1 ' id.
 AD1CON1.5 = 1 ' id
 AD1CON1.4 = 0 ' SSRCG
 AD1CON1.2 = 1 ' sampling immediately after last conversion. SAMP bit it autoset.
 AD1CON2.15 = 0 ' ref AvDD and AsSS
 AD1CON2.14 = 0
 AD1CON2.13 = 0
 AD1CON2.10 = 0 ' no scan
 ' bits 6-2 = 0 ==> generates interrupt after every sample conversion
 AD1CON2.1 = 0 ' always fill buffer from the start adres
 AD1CON2.0 = 0 ' use channel input selects for sample MUXA
 AD1CON3.0 = 0 ' clock derived from system clock
 AD1CON3.12 = 1 ' 10000 = 16 Tad -autosample time bits
 AD1CON3.11 = 0 ' /
 AD1CON3.10 = 0 '/
 AD1CON3.9 = 0 ' /
 AD1CON3.8 = 0 '/
 AD1CON3.Byte0 = 16 ' ADCS ADC1 conversion clock select bits (sampling rate)
 AD1CON4.8 = 0 ' no DMA - results stored in ADC1BUF0 to ADC1BUFF registers
 AD1CHS0 = 0 ' clear complete register. AN0 is input channel
 ' now we have to enable the interrupt and find out how to transfer data to an array
 IEC0.13 = 1 ' enable IRQ
 'IPC3 <6:4> set the priority level
 IFS0.13 = 0 ' clear interrupt flag
 ' ---------------------------------------------------------------------------------
$endif

$ifdef Enable_PWM
 ' PWM channel initialisation ------------------------------------------------------
 'CNPD1 ' enable internal pull down resistor to reset the FLT32 flag on init
  ' disable interrupts:
 IEC5.14 = 0
 IEC5.15 = 0
 IEC6.0 = 0
 ' clear interrupt flags:
 Clear IFS5.14
 Clear IFS5.15
 Clear IFS6.0

 ' pwm time base control register: PTCON
 'PTCON.pwm
 Clear PTCONbits_PTEN ' = PTCON.15 = 0 ' pwmx disabled for setting the bits, should be enabled at the end. PTEN
  'PTCON Timebase control register
 Clear PTCONbits_PTSIDL ' = PTCON.13
 ' PTCONbits_SESTAT 'PTCON.12 ' status bit to read
 Clear PTCONbits_SEIEN ' PTCON.11 disable special event interrupt
 'Set PTCONbits_EIPU ' PTCON.10 1 = active period register is updated immediately
 Clear PTCONbits_EIPU ' PTCON.10 0 = active period register updates occur on PWMx cycle boundaries : setting changed 09.10.2016
 Clear PTCONbits_SYNCPOL ' PTCON.9 sync active high. Irrelevant here as we do not use sync
 Clear PTCONbits_SYNCOEN ' PTCON.8 = 0 ' disable sync output
 Clear PTCONbits_SYNCEN ' PTCON.7 = 0 ' no external sync
 Clear PTCONbits_SYNCSRC0 'PTCON.4
 Clear PTCONbits_SYNCSRC1 'PTCON.5
 Clear PTCONbits_SYNCSRC2 'PTCON.6
 Clear PTCONbits_SEVTPS0 'PTCON.0 special event postscaler bits
 Clear PTCONbits_SEVTPS1 'PTCON.1
 Clear PTCONbits_SEVTPS2 'PTCON.2
 Clear PTCONbits_SEVTPS3 'PTCON.3
    '%110 = / 64
    ' timing resolution should become 64x8.5ns = 544ns = 0.544us

' PTPER register primary master time base period register
 'PTPER = 64 '32678 ' master time base period register --> PWM frequency 16-bits
        ' 1 unit is 8.33ns with a 60MHz Fcy
        ' so 32678 would give 3673 Hz
Select Case PWMmodus
       Case 0
        ' this works o.k. now
        'PWMCON1.9 = 0 ' ITB: Independent time base mode if set to 1
        'PWMCON2.9 = 0 ' PTPER register steers time base if set to 0
        'PWMCON3.9 = 0 ' we do not have a SPHASE1, 2, 3 register thus independent pwm control is not possible
        ' cfr manual example 14-14, p.44
        Clear PWMCON1
        Clear PWMCON2
        Clear PWMCON3
        ' PTCON2 register
        ' pwm input clock prescaler, set to 1 (no division)
        'Set PTPER ' set to lowest frequency = 1831,16 Hz
        ' for the ADSR implementation we should set this as fast as possible!
        'PTPER = 1024 ' 256 '1024 ' would this limit the useable range for PWM values???
        ' 1024 gives a pwm base frequency of 117kHz
        ' 09.10.2016 experiment: try this
        PTPER = 4096 ' it gives 29kHz base freq. for PWM
        Clear PTCON2bits_PCLKDIV0 ' PTCON2.0 ' bit0
        Clear PTCON2bits_PCLKDIV1 ' PTCON2.1 ' bit1
        Clear PTCON2bits_PCLKDIV2 ' PTCON2.2 ' bit2
        Clear PDC1
        Clear PDC2
        Clear PDC3
        Clear PHASE1
        Clear PHASE2
        Clear PHASE3
        Set MDC ' set to longest period

        ' make the pwmL port free for general I/O: (note_Ports)
        IOCON1.15 = 1
        IOCON1.14 = 0
        IOCON2.15 = 1
        IOCON2.14 = 0
        IOCON3.15 = 1
        IOCON3.14 = 0

        ' the FCLCON1,2,3 and IOCON1,2,3 require a key to be written:
        ' pwm channel 1: --------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON1 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON1
        ' set pwm ownership and polarity to IOCON1
        ' IOCON1 = 0xC000 sets pwm mode to complementary outputs
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0x8000, w0 ' required value for IOCON1 ' 0xA800
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON1

        ' pwm channel 2: --------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON2 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON2
        ' set pwm ownership and polarity to IOCON2
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0x8000, w0 ' required value for IOCON2
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON2

        ' pwm channel 3: -----------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON3 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON3
        ' set pwm ownership and polarity to IOCON1
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0x8000, w0 ' required value for IOCON3
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON3
        ' now we have ports free for the timer-tone generators:
        Symbol Note_Port1 PORTB.15
        Symbol Note_Port2 PORTB.13
        Symbol Note_Port3 PORTB.11
        Output Note_Port1
        Output Note_Port2
        Output Note_Port3

       Case 1
        ' cfr. example 14-18, p.48 in manual
        'PWMCON1.9 = 1 ' ITB: Independent time base mode if set to 1
        'PWMCON2.9 = 1 ' PTPER register steers time base if set to 0
        'PWMCON3.9 = 1 ' we do not have a SPHASE1, 2, 3 register thus independent pwm control is not possible
        ' IOCON1,2,3 must be $C000
        PWMCON1 = $0200
        PWMCON2 = $0200
        PWMCON3 = $0200
        ' PTCON2 register
        ' pwm input clock prescaler, set to /64
        Clear PTCON2bits_PCLKDIV0 ' PTCON2.0 ' bit0
        Set PTCON2bits_PCLKDIV1 ' PTCON2.1 ' bit1
        Set PTCON2bits_PCLKDIV2 ' PTCON2.2 ' bit2
        Set PTPER '= 256 ' test value - probably irrelevant in this mode
        Set PHASE1 ' freq to lowest
        Set PHASE2
        Set PHASE3
        Clear PDC1 ' duty cycles note: PDC1 < PHASE1
        Clear PDC2
        Clear PDC3
        Set MDC ' ? clear mdc - seems irrelevant here
        ' make the pwmL port free for general I/O:
        IOCON1.15 = 1
        IOCON1.14 = 0
        IOCON2.15 = 1
        IOCON2.14 = 0
        IOCON3.15 = 1
        IOCON3.14 = 0
        ' the FCLCON1,2,3 and IOCON1,2,3 require a key to be written:
        ' pwm channel 1: --------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON1 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON1
        ' set pwm ownership and polarity to IOCON1
        ' IOCON1 = 0xC000 sets pwm mode to complementary outputs
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0x8000, w0 ' required value for IOCON1 -pwmL disabled.
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON1

        ' pwm channel 2: --------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON2 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON2
        ' set pwm ownership and polarity to IOCON2
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0x8000, w0 ' required value for IOCON2
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON2

        ' pwm channel 3: -----------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON3 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON3
        ' set pwm ownership and polarity to IOCON1
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0x8000, w0 ' required value for IOCON3
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON3
        ' now we have ports free for ADRS:
        Symbol ADSR_Port1 PORTB.15
        Symbol ADSR_Port2 PORTB.13
        Symbol ADSR_Port3 PORTB.11
        Output ADSR_Port1
        Output ADSR_Port2
        Output ADSR_Port3

       Case 2 ' 3-phase motor control setting
        ' ref. ,manual 14-16, p. 46
        'PWMCON1.9 = 0 ' ITB: Independent time base mode if set to 1
        'PWMCON2.9 = 0 ' PTPER register steers common time base if set to 0
        'PWMCON3.9 = 0
        PWMCON1 = $0100
        PWMCON2 = $0100
        PWMCON3 = $0100
        ' PTCON2 register
        ' pwm input clock prescaler, set to /64
        Clear PTCON2bits_PCLKDIV0 ' PTCON2.0 ' bit0
        Set PTCON2bits_PCLKDIV1 ' PTCON2.1 ' bit1
        Set PTCON2bits_PCLKDIV2 ' PTCON2.2 ' bit2
        Clear MDC ' master duty cycle control - set to zero on init
        Set PTPER ' lowest freq.
        Clear PHASE1 ' 0 graden
        PHASE2 = 21845 ' 120 graden
        PHASE3 = 43690 ' 240 graden
        ' the FCLCON1,2,3 and IOCON1,2,3 require a key to be written:
        ' pwm channel 1: --------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON1 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON1
        ' set pwm ownership and polarity to IOCON1
        ' IOCON1 = 0xC000 sets pwm mode to complementary outputs
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC000, w0 ' required value for IOCON1
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON1

        ' pwm channel 2: --------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON2 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON2
        ' set pwm ownership and polarity to IOCON2
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC000, w0 ' required value for IOCON2
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON2

        ' pwm channel 3: -----------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON3 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON3
        ' set pwm ownership and polarity to IOCON1
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC000, w0 ' required value for IOCON3
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON3

      Case 3 ' 2-phase ac motor
        PWMCON1 = $0100
        PWMCON2 = $0100
        Clear PTcon2bits_PCLKDIV0
        Set PTcon2bits_PCLKDIV1
        Set PTcon2bits_PCLKDIV2
        Clear MDC
        Set PTPER
        Clear PHASE1
        PHASE2 = 16384 ' 90 graden
        ' the FCLCON1,2,3 and IOCON1,2,3 require a key to be written:
        ' pwm channel 1: --------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON1 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON1
        ' set pwm ownership and polarity to IOCON1
        ' IOCON1 = 0xC000 sets pwm mode to complementary outputs
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC000, w0 ' required value for IOCON1
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON1

        ' pwm channel 2: --------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON2 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON2
        ' set pwm ownership and polarity to IOCON2
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC000, w0 ' required value for IOCON2
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON2

        ' pwm channel 3: -----------------------------------------------
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC003, w0 ' required value for FCLCON3 ' %1100000000000000 = &HC000
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, FCLCON3
        ' set pwm ownership and polarity to IOCON1
        Mov #0xabcd, w10 ' etc... p. 226 pwm manual
        Mov #0x4321, w11
        Mov #0xC000, w0 ' required value for IOCON3
        Mov w10, PWMKEY
        Mov w11, PWMKEY
        Mov w0, IOCON3
 EndSelect

 ' common settings:

 PWMCON1.12 = 0 'fault interrupt disabled
 PWMCON2.12 = 0
 PWMCON3.12 = 0
 PWMCON1.11 = 0 'current limit disabled
 PWMCON2.11 = 0
 PWMCON3.11 = 0
 PWMCON1.10 = 0 'trigger event interrupts disabled
 PWMCON2.10 = 0
 PWMCON3.10 = 0

' PWMCON1.9 = 1 ' ITB: Independent time base mode if set to 1
' PWMCON2.9 = 1 ' PTPER register steers time base if set to 0
' PWMCON3.9 = 1 ' we do not have a SPHASE1, 2, 3 register thus independent pwm control is not possible

' PWMCON1.8 = 0 'PCD1 en SDC1 registers provide duty cycle info -
' PWMCON2.8 = 0
' PWMCON3.8 = 0
 PWMCON1.7 = 1 ' dead time disabled
 PWMCON2.7 = 1
 PWMCON3.7 = 1
' PWMCON1.6 = 0
' PWMCON2.6 = 0
' PWMCON3.6 = 0
' PWMCON1.3 = 0
' PWMCON2.3 = 0
' PWMCON3.3 = 0
' PWMCON1.2 = 0 ' edge aligned mode CAM bit. Ignored when ITB = 0
' PWMCON2.2 = 0
' PWMCON3.2 = 0
' PWMCON1.1 = 0
' PWMCON2.1 = 0
' PWMCON3.1 = 0
' PWMCON1.0 = 1
' PWMCON2.0 = 1
' PWMCON3.0 = 1
' The pwm1 to pwm3 values for the duty cycle are in the PDC1, PDC2 and PDC3 registers
' The phases in the PHASE1, PHASE2, PHASE3 registers, if not used for frequency.
 AUXCON1 = 0
 AUXCON2 = 0
 AUXCON3 = 0
 Set PTCONbits_PTEN ' = PTCON.15 pwmx should be enabled at the end.
 $endif
 ' ---------------------------------------------------------------------------------

 Variables:
 ' variable declarations:
 ' variables for midi reception and parsing:
    Dim inByte As Byte
    Dim IndexIn As Byte ' Pointer to the next empty location in the buffer
    Dim IndexOut As Byte ' Pointer to the location of the oldest character in the buffer
    Dim Ringbuffer[256] As Byte ' Array for holding received characters in the uart
    Dim Outbuffer[265] As Byte ' buffer for midi-output UART
    Dim OutIdxIn As Byte
    Dim OutIdxOut As Byte
    Dim Bytein As Byte ' midi byte read from buffer
    Dim StBit As Bytein.7 ' highest bit of ByteIn
    ' midi variables
    Dim statusbyte As Byte
    Dim noteUit As Byte ' note off + release value
    Dim release As Byte
    Dim noteAan As Byte ' note on + release value
    Dim velo As Byte
    Dim notePres As Byte ' note pressure + pressure value
    Dim pres As Byte
    Dim Ctrl As Byte ' continuous controller + value
    Dim value As Byte
    Dim prog As Byte ' program change + program-byte
    Dim aft As Byte ' channel aftertouch
    Dim pblsb As Byte ' pitch bend lsb
    Dim pbmsb As Byte ' pitch bend msb
    ' variables for the timing system:
    Dim time As Dword ' 10 us resolution
    Dim maxtim As time.31 ' overflow bit, will cause timer reset after 6 hours
    Dim t As Word ' loopcounter 750kHz
    Dim tl As t.Byte0
    Dim th As t.Byte1
    Dim i As Byte
    Dim j As Word
    Dim idx As Byte
    Dim Nxt As Dword
    Dim TimVals[NrTasks] As Dword
    Dim tg As Bit
    Dim resort_flag As Bit
    Dim Dur[128] As Word
    Dim Dur5[128] As Word
    Dim DataBuffer[256] As Word ' adc databuffer
    Dim DataInIdx As Byte
    Dim DataOutIdx As Byte

    ' 16 bit variables and floats for the PWM system
    Dim pwm1value As Word
    Dim pwm2value As Word
    Dim pwm3value As Word
    Dim pwm1freq As Word
    Dim pwm2freq As Word
    Dim pwm3freq As Word
    Dim pwm1phase As Word
    Dim pwm2phase As Word
    Dim pwm3phase As Word
 ' Dim dutcy1 As Float
 ' Dim dutcy2 As Float
 ' Dim dutcy3 As Float
    ' for integer coding of the duty cycle ctrl. [10.10.2016]
    Dim bdutcy1 As Byte ' 1-128
    Dim bdutcy2 As Byte
    Dim bdutcy3 As Byte

    Dim Period[128] As Word ' midi note lookup table
    ' variables for the ADSR system:
    Dim Attack1_time As Word
    Dim Attack1_level As Word ' derived from velo, with a log-map
    Dim Decay1_time As Word
    Dim Sustain1_level As Word ' derived from volume controller ctrl7, with log-map
    Dim Release1_Time As Word ' derived from release bit with noteoff commands

    Dim Attack2_time As Word
    Dim Attack2_level As Word ' derived from velo, with a log-map
    Dim Decay2_time As Word
    Dim Sustain2_level As Word ' derived from volume controller ctrl7, with log-map
    Dim Release2_Time As Word ' derived from release bit with noteoff commands

    Dim Attack3_time As Word
    Dim Attack3_level As Word ' derived from velo, with a log-map
    Dim Decay3_time As Word
    Dim Sustain3_level As Word ' derived from volume controller ctrl7, with log-map
    Dim Release3_Time As Word ' derived from release bit with noteoff commands

    Dim ADSR1_flags As Byte
    ' more logical arrangement, in time order:
    Dim Attack1_flag As ADSR1_flags.0
    Dim Attack1_tog As ADSR1_flags.1
    Dim Decay1_flag As ADSR1_flags.2
    Dim Decay1_tog As ADSR1_flags.3
    Dim Sustain1_flag As ADSR1_flags.4
    Dim Sustain1_tog As ADSR1_flags.5
    Dim Release1_flag As ADSR1_flags.6
    Dim Release1_tog As ADSR1_flags.7

    Dim cnt1 As Byte 'Word
    Dim Astepval1 As Word
    Dim Dstepval1 As Word
    Dim Rstepval1 As Word

    Dim ADSR2_flags As Byte
    Dim Attack2_flag As ADSR2_flags.0
    Dim Attack2_tog As ADSR2_flags.1
    Dim Decay2_flag As ADSR2_flags.2
    Dim Decay2_tog As ADSR2_flags.3
    Dim Sustain2_flag As ADSR2_flags.4
    Dim Sustain2_tog As ADSR2_flags.5
    Dim Release2_flag As ADSR2_flags.6
    Dim Release2_tog As ADSR2_flags.7

    Dim cnt2 As Byte
    Dim Astepval2 As Word
    Dim Dstepval2 As Word
    Dim Rstepval2 As Word

    Dim ADSR3_flags As Byte
    Dim Attack3_flag As ADSR3_flags.0
    Dim Attack3_tog As ADSR3_flags.1
    Dim Decay3_flag As ADSR3_flags.2
    Dim Decay3_tog As ADSR3_flags.3
    Dim Sustain3_flag As ADSR3_flags.4
    Dim Sustain3_tog As ADSR3_flags.5
    Dim Release3_flag As ADSR3_flags.6
    Dim Release3_tog As ADSR3_flags.7

    Dim cnt3 As Byte
    Dim Astepval3 As Word
    Dim Dstepval3 As Word
    Dim Rstepval3 As Word

    Dim Ont[128] As Word ' on-time lookup for pwm
    Dim Oft[128] As Word ' off-time lookup for pwm - not used in this coding.
    Dim On1 As Word ' for timer1 --> note1
    Dim Of1 As Word
    Dim On2 As Word ' for timer4 --> note2
    Dim Of2 As Word
    Dim On3 As Word ' for timer5 --> note3
    Dim Of3 As Word

    Dim C1bit As Byte ' 13.10.2016
    Dim C1val As Word 'byte ' controller #1 0-127
    Dim jitter As SWord ' random byte -128 -> 127, changed to word 13.10.2016

 Variable_Inits:
      Clear Ringbuffer ' Rx
      Clear IndexIn ' Clear the buffer internal pointer
      Clear IndexOut ' Clear the buffer external pointer
      Clear time
      Clear t
      Clear Outbuffer ' Tx
      Clear OutIdxIn
      Clear OutIdxOut
      Set TimVals
      Clear DataBuffer ' ADC
      Clear DataInIdx
      Clear DataOutIdx
      GoSub Dur_Lookup
      GoSub Period_Lookup_Table
      GoSub PWM_Lookup_Table_60dB ' 10.10.2016, was 60dB lookup before...
        ' different tables available
      GoSub Controller_Init_Prog0 'default controller settings un startup:

GoTo MAIN ' jump over irq's

Interrupt_handling:
' -------------------
 Isr- T1Interrupt ' timer1 interrupt
    Clear IFS0bits_T1IF ' Reset the Timer1 interrupt flag
        ' used for pitch generator1
    Clear TMR1 ' this is required!
    If Note_Port1 = 0 Then
       PR1 = On1
       Set Note_Port1
    Else
       'PR1 = Of1 ' if we want jitter, we should modulate this value
       'PR1.C1bit = TMR2.0 ' pneudo-random
       'PR1.byte0 = PR1.Byte0 ^ jitter ' xor mask
        ' also possible:
        ' PR1.byte0 = PR1.Byte0 ^ TMR2.byte0
       ' better:
       'PR1.Byte0 = PR1.Byte0 - jitter
       ' easier:
       PR1 = Of1 - jitter
       Clear Note_Port1
    EndIf
 EndIsr- ' exit the interrupt

 Isr- T3Interrupt
    Clear IFS0bits_T3IF ' 32-bit value reached (T2/T3 combined)
        ' this is our main timer!
 EndIsr-

 Isr- T4Interrupt
    Clear IFS1bits_T4IF '16-bit value reached
    Clear TMR4
    If Note_Port2 = 0 Then
        PR4 = On2
        Set Note_Port2
    Else
        'PR4 = Of2
        'PR4.C1bit = TMR2.0 ' pneudo-random
        'PR4.byte0 = PR4.Byte0 ^ jitter
        PR4 = Of2 - jitter
        Clear Note_Port2
    EndIf
 EndIsr-

 Isr- T5Interrupt
    Clear IFS1bits_T5IF ' 32-bit value reached if T4/T5 operation ib 32 bits
        ' 16-bit value reached if operated alone.
    Clear TMR5
    If Note_Port3 = 0 Then
        PR5 = On3
        Set Note_Port3
    Else
        'PR5 = Of3
        'PR5.C1bit = TMR2.0 ' pneudo-random
        'PR5.Byte0 = PR5.Byte0 ^ jitter
        PR5 = Of3 - jitter
        Clear Note_Port3
    EndIf
 EndIsr-

 Isr- U1RXInterrupt ' UART receive IRQ - midi receiver
    Clear IFS0.11 ' reset UART1 receive irq flag
    Inc IndexIn ' Move up the buffer index (0-255)
    Ringbuffer[IndexIn] = U1RXREG
    'Toggle midi_led 'debug
 EndIsr-

 Isr- U1ErrInterrupt
    ' this irq is generated on UART1 receive errors
    ' this interrupt is enabled by setting IEC4.1
     ' error handling:
     Clear IFS4.1 ' clear interrupt flag
     If U1STA.2 = 1 Then
       'Set framing_error_led ' no longer happening
     EndIf
     If U1STA.1 = 1 Then ' = overrun error
       'Set overrun_error_led ' not happening
       Clear U1STA.1
     EndIf
 EndIsr-

 Isr- U1TXInterrupt ' UART send IRQ
    Clear IFS0bits_U1TXIF ' reset UART1 transmit IRQ flag
    'Toggle midi_led ' transmit monitor
 EndIsr-

 Isr- AD1Interrupt
     ' this irq happens after every ADC conversion
     Clear IFS0.13 ' clear interrupt flag
     Inc DataInIdx ' move up the buffer index
     DataBuffer[DataInIdx] = ADC1BUF0 ' loopt tot ADC1BUFF -so 16 words deep
     Toggle PORTA.1 ' for testing sampling rate - 04.08.2016: gives 58.82 kHz
        ' this means 8.5 us for each conversion
 EndIsr-

 Isr- PWM1Interrupt
     Clear IFS5.14
 EndIsr-

 Isr- PWM2Interrupt
     Clear IFS5.15
 EndIsr

 Isr- PWM3Interrupt
     Clear IFS6.0
 EndIsr-

GetMidi:
    If IndexIn <> IndexOut Then
        Inc IndexOut
        Bytein = Ringbuffer[IndexOut]
    Else
        Set Bytein
    EndIf
Return

GetADC:
    ' here we can perform data extraction and signal conditioning
    ' the data-buffer has 256 words and covers 2.176ms of time.
Return

 MAIN:
 While
        ' timer23 version: ' overflows after 5 hours.
        time.Word0 = TMR2 ' time is a dword var
        time.Word1 = TMR3 ' resolution is 4.224 us

$ifdef Enable_UART_RX ' if receiver is enabled
        GoSub GetMidi ' Read data from the serial buffer
        ' Start the midi parser.
        Midi_Parse:
        If Bytein > ProgChange_Status Then ' here higher statusses are not implemented.
        If Bytein > 253 Then '254 = midiclock, 255= reset
        'midiclock can interrupt all other msg's...
        '255 had to be intercepted since thats what we
        'get when no new byte flows in.
        Else
        Clear statusbyte 'reset the status byte
        EndIf
        GoTo Midi_Parse_done 'throw away...
        EndIf
        If StBit =1 Then 'should be faster than If Bytein > 127 Then
        'status byte received, bit 7 is set
        Clear statusbyte 'if on another channel, the statusbyte needs a reset
        Select Bytein 'eqv to Select case ByteIn
        Case NoteOff_Status
        statusbyte = Bytein
        Set noteUit 'reset value. Cannot be 0 !!!
        Set release '0 is a valid midi note!
        Case NoteOn_Status
        statusbyte = Bytein
        Set noteAan '= 255
        Set velo '= 255
        Case Keypres_Status
        statusbyte = Bytein
        Set notePres '= 255
        Set pres '= 255
        Case Control_Status ' controllers and switches
        statusbyte = Bytein
        Set Ctrl
        Set value
        Case ProgChange_Status
        statusbyte = Bytein
        Set prog '= 255
' Case Aftertouch_Status ' not used on this board
' statusbyte = Bytein
' Set aft
' Case Pitchbend_Status
' statusbyte = Bytein
' Set pblsb '= 255
' Set pbmsb '= 255
        EndSelect
        Else 'midi byte is 7 bits
        Select statusbyte
        Case 0 'not a message for this channel
        GoTo Midi_Parse_done 'Check_Timers 'disregard
        Case NoteOff_Status
        If noteUit = 255 Then
        noteUit = Bytein
        Else
        release = Bytein
'message complete, so we can do the action...
        Select noteUit

' coding with 3 ADRS's and fixed pwm channels
        Case note1, note1o, note1o2, note1o3
        Clear ADSR1_flags
' reset all flags = 0
        If release > 0 Then
        Release1_Time = release << ADSR_shift
  ' so if CC23 = release time was set, we use it
        EndIf
        If Release1_Time > 0 Then
        Set Release1_flag
' clear PDC1 performed at the end of the release cycle = 64
        Rstepval1 = Release1_Time / (Sustain1_level + 1 )
        ' sustain_level mag niet 0 zijn!
        TimVals[4] = time + Rstepval1
        Else
        ' perform a noteoff - no release phase
        Set TimVals[4]
' cancel timer
        Clear PDC1
' stop adsr - volume to zero
        Clear IEC0bits_T1IE
' disable timer1 interrupt - now tone generator
        Clear IFS0bits_T1IF
' clear interrupt flag
        Clear Note_Port1
        EndIf
        Set resort_flag
        Case note2, note2o, note2o2, note2o3
' =23, 35
        Clear ADSR2_flags
        If release > 0 Then
        Release2_Time = release << ADSR_shift ' so if CC29 = release time was set, we use it
        EndIf
        If Release2_Time > 0 Then
        Set Release2_flag ' clear PDC2 performed at the end of the release cycle
        Rstepval2 = Release2_Time / (Sustain2_level + 1)
        TimVals[5] = time + Rstepval2
        Else
        ' perform a noteoff - no release phase
        Set TimVals[5]
        Clear PDC2 ' stop adsr
        Clear IEC1bits_T4IE ' disable timer4 interrupt
        Clear IFS1bits_T4IF ' clear interrupt flag
        Clear Note_Port2
        EndIf
        Set resort_flag
        Case note3, note3o, note3o2, note3o3 ' =24, 36 , 48 , 60
        Clear ADSR3_flags
        If release > 0 Then
        Release3_Time = release << ADSR_shift ' so if CC39 = release time was set, we use it
        EndIf
        If Release3_Time > 0 Then
        Set Release3_flag ' clear PDC3 performed at the end of the release cycle
        Rstepval3 = Release3_Time / (Sustain3_level + 1)
        TimVals[6] = time + Rstepval3
        Else
        ' perform a noteoff - no release phase
        Set TimVals[6]
        Clear PDC3 ' stop volume
        Clear IEC1bits_T5IE ' disable timer5 interrupt
        Clear IFS1bits_T5IF ' clear interrupt flag
        Clear Note_Port3
        EndIf
        Set resort_flag
        EndSelect
        Set noteUit 'reset
        EndIf
        Case NoteOn_Status
        If noteAan = 255 Then
        noteAan = Bytein
        Else
        velo = Bytein
        If velo = 0 Then ' note off via velo=0
        Select noteAan
        Case note1, note1o, note1o2, note1o3 ' =22, 34
        Clear ADSR1_flags
        If Release1_Time > 0 Then
        Set Release1_flag ' clear PDC1 performed at the end of the release cycle
        Rstepval1 = Release1_Time / (Sustain1_level + 1)
        TimVals[4] = time + Rstepval1
        Else
        ' perform a noteoff - no release phase
        Set TimVals[4] ' clear timer
        Clear PDC1 ' stop volume
        Clear IEC0bits_T1IE ' disable timer1 interrupt
        Clear IFS0bits_T1IF ' clear interrupt flag
        Clear Note_Port1
        EndIf
        Set resort_flag
        Case note2, note2o, note2o2, note2o3 '= 23 , 35
        Clear ADSR2_flags
        If Release2_Time > 0 Then
        Set Release2_flag ' clear PDC2 performed at the end of the release cycle
        Rstepval2 = Release2_Time / (Sustain2_level + 1)
        TimVals[5] = time + Rstepval2
        Else
        ' perform a noteoff - no release phase
        Set TimVals[5]
        Clear PDC2 ' stop tone
        Clear IEC1bits_T4IE ' disable timer4 interrupt
        Clear IFS1bits_T4IF ' clear interrupt flag
        Clear Note_Port2
        EndIf
        Set resort_flag
        Case note3, note3o, note3o2, note3o3 '= 24, 36
        Clear ADSR3_flags
        If Release3_Time > 0 Then
        Set Release3_flag ' clear PDC3 performed at the end of the release cycle
        Rstepval3 = Release3_Time / (Sustain3_level + 1)
        TimVals[6] = time + Rstepval3
        Else
        ' perform a noteoff - no release phase
        Set TimVals[6]
        Clear PDC3 ' stop
        Clear IEC1bits_T5IE ' disable timer5 interrupt
        Clear IFS1bits_T5IF ' clear interrupt flag
        Clear Note_Port3
        EndIf
        Set resort_flag
        EndSelect
        Else
        Select noteAan
        Case note1
        Attack1_level = velo ' here velo is always > 0
        Clear ADSR1_flags ' added 10.10.2016
        ' program timer1 as frequency generator
        On1 = note1_period.Byte1 * bdutcy1
        Of1 = note1_period - On1
        Clear Note_Port1
        Clear IFS0bits_T1IF
        Set IEC0bits_T1IE
        ' now use the pwm1 channel for the ADSR
        Clear PDC1 ' start from volume = 0
        Attack1_flag =
        Astepval1 = Attack1_time / Attack1_level
     ' start faze 1 van de ADSR
        ' bereken alvast de waarden die na de attack moeten volgen:
        If Attack1_level <> Sustain1_level Then
        Dstepval1 = Decay1_time / Abs(Attack1_level - Sustain1_level)
        Else
        Clear Dstepval1
        EndIf
        TimVals[4] = time + Astepval1
        Set resort_flag
        Case note2
        Attack2_level = velo
        Clear ADSR2_flags
        ' program timer4 as frequency generator
        On2 = note2_period.Byte1 * bdutcy2
    ' Period[noteAan] * dutcy2
        Of2 = note2_period - On2	' Period[noteAan] - On2
        Clear IFS1bits_T4IF
' clear irq flag
        Set IEC1bits_T4IE
' enable timer4 interrupt
        Clear Note_Port2
        ' now use the pwm2 channel for the ADSR
        Clear PDC2
' start from volume = 0
        Attack2_flag = 1
'Set Attack2_flag
        Astepval2 = Attack2_time / Attack2_level
        If Attack2_level <> Sustain2_level Then
        Dstepval2 = Attack2_time / Abs(Attack2_level - Sustain2_level)
        Else
        Clear Dstepval2
        EndIf
        TimVals[5] = time + Astepval2
        Set resort_flag
        Case note3
        Attack3_level = velo
        Clear ADSR3_flags
        ' program timer5 as frequency generator
        On3 = note3_period.Byte1 * bdutcy3 ' Period[noteAan] * dutcy3
        Of3 = note3_period - On3 ' Period[noteAan] - On3
        Clear IFS1bits_T5IF ' clear irq flag
        Set IEC1bits_T5IE ' enable timer5 interrupt
        Clear Note_Port3
        ' now use the pwm3 channel for the ADSR
        'Clear ADSR3_flags ' start new cycle
        Clear PDC3 ' start from volume = 0
        Attack3_flag = 1 ' =Set Attack3_flag
        Astepval3 = Attack3_time / Attack3_level
        If Attack3_level <> Sustain3_level Then
        Dstepval3 = Attack3_time / Abs(Attack3_level - Sustain3_level)
        Else
        Clear Dstepval3
        EndIf
        TimVals[6] = time + Astepval3
        Set resort_flag
        Case note1o
        Attack1_level = velo ' here velo is always > 0
        Clear ADSR1_flags
        ' program timer1 as frequency generator
        On1 = note1o_period.Byte1 * bdutcy1
        Of1 = note1o_period - On1
        Clear Note_Port1
        Clear IFS0bits_T1IF ' clear irq flag
        Set IEC0bits_T1IE ' enable timer1 interrupt
        ' now use the pwm1 channel for the ADSR
        Clear PDC1 ' start from volume = 0
        Attack1_flag = 1 ' Set Attack1_flag ' = 1
        Astepval1 = Attack1_time / Attack1_level ' start faze 1 van de ADSR
        ' bereken alvast de waarden die na de attack moeten volgen:
        If Attack1_level <> Sustain1_level Then
        Dstepval1 = Decay1_time / Abs(Attack1_level - Sustain1_level)
        Else
        Clear Dstepval1
        EndIf
        TimVals[4] = time + Astepval1
        Set resort_flag
        Case note2o
        Attack2_level = velo
        Clear ADSR2_flags
        ' program timer4 as frequency generator
        On2 = note2o_period.Byte1 * bdutcy2 ' Period[noteAan] * dutcy2
        Of2 = note2o_period - On2 ' Period[noteAan] - On2
        Clear IFS1bits_T4IF ' clear irq flag
        Set IEC1bits_T4IE ' enable timer4 interrupt
        Clear Note_Port2
        ' now use the pwm2 channel for the ADSR
        Clear PDC2 ' start from volume = 0
        Attack2_flag = 1 'Set Attack2_flag
        Astepval2 = Attack2_time / Attack2_level
        If Attack2_level <> Sustain2_level Then
        Dstepval2 = Attack2_time / Abs(Attack2_level - Sustain2_level)
        Else
        Clear Dstepval2
        EndIf
        TimVals[5] = time + Astepval2
        Set resort_flag
        Case note3o
        Attack3_level = velo
        Clear ADSR3_flags
        ' program timer5 as frequency generator
        On3 = note3o_period.Byte1 * bdutcy3 ' Period[noteAan] * dutcy3
        Of3 = note3o_period - On3 ' Period[noteAan] - On3
        Clear IFS1bits_T5IF ' clear irq flag
        Set IEC1bits_T5IE ' enable timer5 interrupt
        Clear Note_Port3
        ' now use the pwm3 channel for the ADSR
        Clear PDC3 ' start from volume = 0
        Attack3_flag = 1 ' =Set Attack3_flag
        Astepval3 = Attack3_time / Attack3_level
        If Attack3_level <> Sustain3_level Then
        Dstepval3 = Attack3_time / Abs(Attack3_level - Sustain3_level)
        Else
        Clear Dstepval3
        EndIf
        TimVals[6] = time + Astepval3
        Set resort_flag
        Case note1o2
        Attack1_level = velo ' here velo is always > 0
        Clear ADSR1_flags
        ' program timer1 as frequency generator
        On1 = note1o2_period.Byte1 * bdutcy1
        Of1 = note1o2_period - On1
        Clear Note_Port1
        Clear IFS0bits_T1IF ' clear irq flag
        Set IEC0bits_T1IE ' enable timer1 interrupt
        ' now use the pwm1 channel for the ADSR
        Clear PDC1 ' start from volume = 0
        Attack1_flag = 1 ' Set Attack1_flag ' = 1
        Astepval1 = Attack1_time / Attack1_level ' start faze 1 van de ADSR
        ' bereken alvast de waarden die na de attack moeten volgen:
        If Attack1_level <> Sustain1_level Then
        Dstepval1 = Decay1_time / Abs(Attack1_level - Sustain1_level)
        Else
        Clear Dstepval1
        EndIf
        TimVals[4] = time + Astepval1
        Set resort_flag
        Case note2o2
        Attack2_level = velo
        Clear ADSR2_flags
        ' program timer4 as frequency generator
        On2 = note2o2_period.Byte1 * bdutcy2 ' Period[noteAan] * dutcy2
        Of2 = note2o2_period - On2 ' Period[noteAan] - On2
        Clear IFS1bits_T4IF ' clear irq flag
        Set IEC1bits_T4IE ' enable timer4 interrupt
        Clear Note_Port2
        ' now use the pwm2 channel for the ADSR
        Clear PDC2 ' start from volume = 0
        Attack2_flag = 1 'Set Attack2_flag
        Astepval2 = Attack2_time / Attack2_level
        If Attack2_level <> Sustain2_level Then
        Dstepval2 = Attack2_time / Abs(Attack2_level - Sustain2_level)
        Else
        Clear Dstepval2
        EndIf
        TimVals[5] = time + Astepval2
        Set resort_flag
        Case note3o2
        Attack3_level = velo
        Clear ADSR3_flags
        ' program timer5 as frequency generator
        On3 = note3o2_period.Byte1 * bdutcy3 ' Period[noteAan] * dutcy3
        Of3 = note3o2_period - On3 ' Period[noteAan] - On3
        Clear IFS1bits_T5IF ' clear irq flag
        Set IEC1bits_T5IE ' enable timer5 interrupt
        Clear Note_Port3
        ' now use the pwm3 channel for the ADSR
        Clear PDC3 ' start from volume = 0
        Attack3_flag = 1 ' =Set Attack3_flag
        Astepval3 = Attack3_time / Attack3_level
        If Attack3_level <> Sustain3_level Then
        Dstepval3 = Attack3_time / Abs(Attack3_level - Sustain3_level)
        Else
        Clear Dstepval3
        EndIf
        TimVals[6] = time + Astepval3
        Set resort_flag
        Case note1o3
        Attack1_level = velo ' here velo is always > 0
        Clear ADSR1_flags
        ' program timer1 as frequency generator
        On1 = note1o3_period.Byte1 * bdutcy1
        Of1 = note1o3_period - On1
        Clear Note_Port1
        Clear IFS0bits_T1IF ' clear irq flag
        Set IEC0bits_T1IE ' enable timer1 interrupt
        ' now use the pwm1 channel for the ADSR
        Clear PDC1 ' start from volume = 0
        Attack1_flag = 1 ' Set Attack1_flag ' = 1
        Astepval1 = Attack1_time / Attack1_level ' start faze 1 van de ADSR
        ' bereken alvast de waarden die na de attack moeten volgen:
        If Attack1_level <> Sustain1_level Then
        Dstepval1 = Decay1_time / Abs(Attack1_level - Sustain1_level)
        Else
        Clear Dstepval1
        EndIf
        TimVals[4] = time + Astepval1
        Set resort_flag
        Case note2o3
        Attack2_level = velo
        Clear ADSR2_flags
        ' program timer4 as frequency generator
        On2 = note2o3_period.Byte1 * bdutcy2 ' Period[noteAan] * dutcy2
        Of2 = note2o3_period - On2 ' Period[noteAan] - On2
        Clear IFS1bits_T4IF ' clear irq flag
        Set IEC1bits_T4IE ' enable timer4 interrupt
        Clear Note_Port2
        ' now use the pwm2 channel for the ADSR
        Clear PDC2 ' start from volume = 0
        Attack2_flag = 1 'Set Attack2_flag
        Astepval2 = Attack2_time / Attack2_level
        If Attack2_level <> Sustain2_level Then
        Dstepval2 = Attack2_time / Abs(Attack2_level - Sustain2_level)
        Else
        Clear Dstepval2
        EndIf
        TimVals[5] = time + Astepval2
        Set resort_flag
        Case note3o3
        Attack3_level = velo
        Clear ADSR3_flags
        ' program timer5 as frequency generator
        On3 = note3o3_period.Byte1 * bdutcy3	' Period[noteAan] * dutcy3
        Of3 = note3o3_period - On3	' Period[noteAan] - On3
        Clear IFS1bits_T5IF ' clear irq flag
        Set IEC1bits_T5IE ' enable timer5
        Clear Note_Port3
        ' now use the pwm3 channel for the ADSR
        Clear PDC3
        ' start from volume = 0
        Attack3_flag = 1
        ' =Set Attack3_flag
        Astepval3 = Attack3_time / Attack3_level
        If Attack3_level <> Sustain3_level Then
        Dstepval3 = Attack3_time / Abs(Attack3_level - Sustain3_level)
        Else
        Clear Dstepval3
        EndIf
        TimVals[6] = time + Astepval3
        Set resort_flag
        EndSelect
        Set noteAan '= 255
        EndIf
        EndIf
        Case Keypres_Status
        If notePres = 255 Then
        notePres = Bytein
        Else
        pres = Bytein
        GoSub KeyPres
        EndIf
        Case Control_Status
        If Ctrl = 255 Then
        Ctrl = Bytein
        Else
        value = Bytein
        GoSub Controller
        EndIf
        Case ProgChange_Status
        If prog = 255 Then 'single byte message
        prog = Bytein
        GoSub ProgChange
        EndIf
        Case Aftertouch_Status
        If aft = 255 Then
        aft = Bytein
        GoSub Aftertouch
        EndIf
        Case Pitchbend_Status
        If pblsb = 255 Then
        pblsb = Bytein
        Else
        pbmsb = Bytein
        GoSub Pitchbend
        EndIf
        EndSelect
        EndIf
$endif

Midi_Parse_done:

If resort_flag= 1 Then
    GoSub SortTimers
EndIf

Check_Timers:
If idx < NrTasks Then ' we moeten alleen checken wanneer er een timer loopt
   If time >= Nxt Then ' nagaan of de eerstvolgende timer afgelopen is...
        ' in dit geval is de eerste timer afgelopen en moeten we de juiste aktie
        ' ondernemen:
        Set Nxt.31 ' timer reset, is immers afgelopen
        ' aan de hand van idx weten we welke timer dit is
        Select idx
        Case 4 ' noot1 adsr
        Select ADSR1_flags
        Case 1
        ' if we get here, the first attack steptime has passed
        ' = Attack1_flag
        Clear cnt1
        ADSR1_flags = 2 ' = Attack1_tog
        TimVals[4] = time + Astepval1
        Case 2 ' = Attack1_flag + Attack1_tog
        If cnt1 < Attack1_level Then
        Inc cnt1
        ' increase volume until attack_level reached
        PDC1 = Ont[cnt1]
        TimVals[4] = time + Astepval1
        ' calculated on reception of note-on
        Else ' attack level reached
        Clear ADSR1_flags ' becomes 0
        Select Attack1_level
        Case Sustain1_level
        ' no decay phase required
        Set TimVals[4] ' clear timer
        cnt1 = Sustain1_level
        Case > Sustain1_level
        Set Decay1_flag ' becomes 4
        cnt1= Attack1_level
        ' start value for the decay
        ' steps calculated on reception of note-on
        PDC1 = Ont[cnt1]
        TimVals[4] = time + Dstepval1
        Case Else
        ' attack level <= sustain level
        Set Decay1_tog
        ' further increase flag... becomes 8
        cnt1 = Attack1_level
        PDC1 = Ont[cnt1]
        TimVals[4] = time + Dstepval1
        EndSelect
        EndIf
        Case 4 ' decay flag is set, downwards decay
        Dec cnt1
        PDC1 = Ont[cnt1]
        TimVals[4] = time + Dstepval1
        If cnt1 = Sustain1_level Then
        Clear ADSR1_flags
        ' Decay1_flag becomes 0
        Set TimVals[4] ' cancel the timer
        EndIf
        Case 8
        ' in this case we should increase volume until sustain level is reached
        Inc cnt1
        PDC1 = Ont[cnt1]
        TimVals[4] = time + Dstepval1
        If cnt1 = Sustain1_level Then
        Clear ADSR1_flags 'Decay1_tog
        ' becomes 0
        Set TimVals[4] ' cancel timer
        EndIf
        Case 64
        ' release flag is set - set in the note-off command
        cnt1 = Sustain1_level
        PDC1 = Ont[cnt1]' ? required, added 20.09.2016
        ADSR1_flags = 128 ' Set Release1_tog	' becomes 192 = 128 + 64
        TimVals[4] = time + Rstepval1
        ' stepval calculated at note-off time
        Case 128 ' 192
        ' release-phase
        If cnt1 > 0 Then
        Dec cnt1
        PDC1 = Ont[cnt1]
        TimVals[4] = time + Rstepval1
        Else
        ' if we get here, release time has passed
        Clear ADSR1_flags ' Release1_flag
        Clear PDC1
        ' so we can switch off the volume
        Clear TMR1
        ' stop tone generator
        Clear IEC0bits_T1IE
        ' disable timer1 interrupt
        Clear IFS0bits_T1IF
        ' clear interrupt flag
        Clear Note_Port1 ' zero out
        Set TimVals[4] ' clear timer
        EndIf
        EndSelect
        Case 5 ' noot2 adsr
        Select ADSR2_flags
        Case 1
        ' if we get here, the first attack steptime has passed
        Clear cnt2
        ADSR2_flags = 2 'Set Attack2_tog
        ' now becomes = 3
        TimVals[5] = time + Astepval2
        Case 2
        If cnt2 < Attack2_level Then
        Inc cnt2
        ' increase volume until attack_level reached
        PDC2 = Ont[cnt2]
        TimVals[5] = time + Astepval2
        Else ' attack level reached
        Clear ADSR2_flags ' becomes 0
        If Attack2_level = Sustain2_level Then
        ' no decay phase required
        Set Sustain2_flag ' = 16
        Set TimVals[5]
        cnt2 = Sustain2_level
        EndIf
        If Attack2_level > Sustain2_level Then
        Set Decay2_flag ' becomes 4
        cnt2= Attack2_level
        ' start value for the decay
        PDC2 = Ont[cnt2]
        TimVals[5] = time + Dstepval2
        Else ' attack level <= sustain level
        Set Decay2_tog
        ' further increase flag... becomes 8
        cnt2 = Attack2_level
        PDC2 = Ont[cnt2]
        TimVals[5] = time + Dstepval2
        EndIf
        EndIf
        Case 4 ' decay flag is set
        Dec cnt2
        PDC2 = Ont[cnt2]
        TimVals[5] = time + Dstepval2
        If cnt2 = Sustain2_level Then
        Clear Decay2_flag ' becomes 0
        Set Sustain2_flag
        ' value becomes 16 now
        ' shouldn't we cancel the timer now?
        Set TimVals[5]
        EndIf
        Case 8
        ' in this case we should increase volume until sustain level is reached
        Inc cnt2
        PDC2 = Ont[cnt2]
        TimVals[5] = time + Dstepval2
        If cnt2 = Sustain2_level Then
        Clear Decay2_tog ' becomes 0
        Set Sustain2_flag ' becomes 16
        Set TimVals[5]
        EndIf
        Case 64 ' release flag is set
        cnt2 = Sustain2_level
        PDC2 = Ont[cnt2]
        ADSR2_flags = 128 'Set Release2_tog ' becomes 192
        TimVals[5] = time + Rstepval2
        Case 128 ' release-phase
        If cnt2 > 0 Then
        Dec cnt2
        PDC2 = Ont[cnt2]
        TimVals[5] = time + Rstepval2
        Else ' if we get here, release time has passed
        Clear ADSR2_flags ' Release1_flag
        Clear PDC2 ' so we can switch off the volume
        Clear TMR4 ' stop tone generator
        Clear IEC1bits_T4IE ' disable timer4 interrupt
        Clear IFS1bits_T4IF ' clear interrupt flag
        Clear Note_Port2
        Set TimVals[5]
        EndIf
        EndSelect
        Case 6 ' noot3 adsr
        Select ADSR3_flags
        Case 1 ' if we get here, the first attack steptime has passed
        Clear cnt3
        ADSR3_flags = 2 'Set Attack3_tog ' now becomes = 3
        TimVals[6] = time + Astepval3
        Case 2
        If cnt3 < Attack3_level Then
        Inc cnt3 ' increase volume until attack_level reached
        PDC3 = Ont[cnt3]
        TimVals[6] = time + Astepval3
        Else ' attack level reached
        Clear ADSR3_flags ' becomes 0
        If Attack3_level = Sustain3_level Then ' no decay phase required
        Set Sustain3_flag ' = 16
        Set TimVals[6]
        cnt3 = Sustain3_level
        EndIf
        If Attack3_level > Sustain3_level Then
        Set Decay3_flag ' becomes 4
        cnt3= Attack3_level ' start value for the decay
        PDC3 = Ont[cnt3]
        TimVals[6] = time + Dstepval3
        Else ' attack level <= sustain level
        Set Decay3_tog ' further increase flag... becomes 8
        cnt3 = Attack3_level
        PDC3 = Ont[cnt3]
        TimVals[6] = time + Dstepval3
        EndIf
        EndIf
        Case 4 ' decay flag is set
        Dec cnt3
        PDC3 = Ont[cnt3]
        TimVals[6] = time + Dstepval3
        If cnt3 = Sustain3_level Then
        Clear Decay3_flag ' becomes 0
        Set Sustain3_flag ' value becomes 16 now ' shouldn't we cancel the timer now?
        Set TimVals[6]
        EndIf
        Case 8
        ' in this case we should increase volume
        ' until sustain level is reached
        Inc cnt3
        PDC3 = Ont[cnt3]
        TimVals[6] = time + Dstepval3
        If cnt3 = Sustain3_level Then
        Clear Decay3_tog ' becomes 0
        Set Sustain3_flag ' becomes 16
        Set TimVals[6]
        EndIf
        Case 64 ' release flag is set
        cnt3 = Sustain3_level
        PDC3 = Ont[cnt3]
        ADSR3_flags =
        TimVals[6] = time + Rstepval3
        Case 128 ' release-phase
        If cnt3 > 0 Then
        Dec cnt3
        PDC3 = Ont[cnt3]
        TimVals[6] = time + Rstepval3
        Else ' if we get here, release time has passed
        Clear ADSR3_flags ' Release1_flag
        Clear PDC3 ' so we can switch
        ' off the volume
        Clear TMR5 ' stop generator
        Clear IEC1bits_T5IE ' disable
        Clear IFS1bits_T5IF ' clear interrupt
        Clear Note_Port3
        Set TimVals[6]
        EndIf
        EndSelect
        'Case Else
        ' ' in dit geval is idx geset
        ' GoTo jumpout
        EndSelect
        GoSub SortTimers ' find a new nxt and idx
   EndIf
      ' beveiliging tegen overflow crashes...
      If maxtim = 1 Then
        Clear time
        Clear TMR2
        Clear TMR3
        Set TimVals
      EndIf
Else
      ' no timers running, so to avoid overflows, we can reset the loop timer
      If maxtim = 1 Then
        Clear time ' 16.06.2015
        Clear TMR2 ' 07.08.2016
        Clear TMR3
      EndIf
EndIf

$ifdef Enable_UART_TX ' not defined in this code
Midi_OutPut:
     If OutIdxOut <> OutIdxIn Then
        ' in dit geval is er een byte te versturen
        If IFS0bits_U1TXIF = 0 Then
        Inc OutIdxOut
        U1TXREG = Outbuffer[OutIdxOut]
        EndIf
     EndIf
$endif

jit_algo:
      ' for Ctrl#1 implementation
      j = Random & C1val ' 0 - 254, with mask so range will be 0 - C1val
        ' now 0 - 1023
      jitter = (C1val >> 1) - j ' make it bipolar - 512 -> + 511 ' -128 -> 127

 'Toggle loopcnt ' for loopspeed measurement: 1.3us now
        ' 10.08.2016: 366kHz met alle taken aan, 440kHz onbelast
     watchdog_led = time.16
 Wend

 SortTimers:
        'look up the next smallest timer value in the Timvals array
        ' zoek de de volgende kleinste timer waarde:
        Set idx ' makes it 255
        Set Nxt.31 ' nxt is set on entry. - for speed, we just set the highest bit
        For i = 4 To 6 ' NrTasks - 1 ' we do not use tasks 0-3 nor 7 here 24.08.2016
        If TimVals[i] < Nxt Then
        Nxt = TimVals[i] ' 8 dword comparisons
        idx = i
        EndIf
        Next i
        Clear resort_flag
Return
 ' **************************************************************************************
 ' procedures for midi receiver:
KeyPres:
   ' can be used to modulate the wave shape
    ' 10.10.2016: rewritten avoiding floats...
    Select notePres
        Case note1
        bdutcy1 = pres + 1
        On1 = note1_period.Byte1 * bdutcy1
        Of1 = note1_period - On1
        Case note2
        bdutcy2 = pres + 1
        On2 = note2_period.Byte1 * bdutcy2
        Of2 = note2_period - On2
        Case note3
        bdutcy3 = pres + 1
        On3 = note3_period.Byte1 * bdutcy3
        Of3 = note3_period - On3
        Case note1o
        bdutcy1 = pres + 1
        On1 = note1o_period.Byte1 * bdutcy1
        Of1 = note1o_period - On1
        Case note2o
        bdutcy2 = pres + 1
        On2 = note2o_period.Byte1 * bdutcy2
        Of2 = note2o_period - On2
        Case note3o
        bdutcy3 = pres + 1
        On3 = note3o_period.Byte1 * bdutcy3
        Of3 = note3o_period - On3
        Case note1o2
        bdutcy1 = pres + 1
        On1 = note1o2_period.Byte1 * bdutcy1
        Of1 = note1o2_period - On1
        Case note2o2
        bdutcy2 = pres + 1
        On2 = note2o2_period.Byte1 * bdutcy2
        Of2 = note2o2_period - On2
        Case note3o2
        bdutcy3 = pres + 1
        On3 = note3o2_period.Byte1 * bdutcy3
        Of3 = note3o2_period - On3
        Case note1o3
        bdutcy1 = pres + 1
        On1 = note1o3_period.Byte1 * bdutcy1
        Of1 = note1o3_period - On1
        Case note2o3
        bdutcy2 = pres + 1
        On2 = note2o3_period.Byte1 * bdutcy2
        Of2 = note2o3_period - On2
        Case note3o3
        bdutcy3 = pres + 1
        On3 = note3o3_period.Byte1 * bdutcy3
        Of3 = note3o3_period - On3
    EndSelect
    Set notePres '= 255
Return

ProgChange:
    ' could be implemented to enable or disable common notes with <Hybr>
    ' or for adding presets.
    ' make sure the code in the hub firmware, also sends the program change command!
    ' Presets would also be possible to change the tuning...
    Select prog
        Case 0 'reset controllers to cold boot values
        GoSub Controller_Init_Prog0
        Case 1 ' place for many more presets
        GoSub Preset1
        Case 2
        GoSub Preset2
        Case 3
        GoSub Preset3
        Case 4
        GoSub Preset4
        Case 5
        GoSub Preset5
        Case 6
        GoSub Preset6
        Case 7
        GoSub Preset7
    EndSelect
    Set prog '= 255 'this is not realy required
Return

Pitchbend: ' not implemented
    Set pblsb
    Set pbmsb
Return

Aftertouch:
     'this is the channel aftertouch, affecting any playing note
     'not implemented here.
    Set aft ' reset
Return

Controller:
    Select Ctrl
        Case 1
        'C1bit, C1val - introduced 13.10.2016
        C1val = value << 3 ' 0- 1023 '0-254
        C1bit = Ncd value ' returns 0-8
'Priority encoder of a 16-bit or 32-bit value. Ncd takes a value, finds the highest
' bit containing a 1 and returns the bit position plus one (1 through 32). If no
' bit is set, the input value is 0. Ncd returns 0. Ncd is a fast way to get an answer
' to the question "what is the largest power of two that this value is greater than or
' equal to?" The answer that Ncd returns will be that power, plus one.
        Case 7
        ' global volume controller (in fact, sustain controller)
        'CC7 = value ' needs remapping on a 16-bit log scale
        Sustain1_level = value
        Sustain2_level = value
        Sustain3_level = value
        Case 15
        ' global waveform control - also done for individual notes with keypres
        ' note that using this controller it is not possible to change
        ' the waveform whilst the note is sounding.
        ' If that is required, use the key pressure commands.
        Inc value ' 0 crashes the system...
        bdutcy1 = value ' 1-128
        bdutcy2 = value
        bdutcy3 = value
        Case 17
        ' global attack time control
        Attack1_time = value << ADSR_shift 'CC17
        Attack2_time = Attack1_time
        Attack3_time = Attack1_time
        Case 18
        ' global decay time control
        Decay1_time = value << ADSR_shift ' sustain level set with CC7
        Decay2_time = Decay1_time
        Decay3_time = Decay1_time
        Case 19
        ' global release time control
        Release1_Time = value << Release_Shift 'ADSR_shift
' can also be set with the note-off release value
        Release2_Time = Release1_Time
        Release3_Time = Release1_Time
        'Case 20
        ' should be tuning
        Case Att1 '21
        ' for note 22 only
        Attack1_time = value << ADSR_shift
        Case Decr1 '22
        ' for note 22 only
        Decay1_time = value << ADSR_shift
        Case Rel1 '23
        ' for note 22 only
        Release1_Time = value << Release_Shift 'ADSR_shift
        Case Att2 '24
        ' for note 23 only
        Attack2_time = value << ADSR_shift
        Case Decr2 '25
        ' for note 23 only
        Decay2_time = value << ADSR_shift
        Case Rel2 '26
        ' for note 23 only
        Release2_Time = value << Release_Shift 'ADSR_shift
        Case Att3 '27
        ' for note 24 only
        Attack3_time = value << ADSR_shift
        Case Decr3 '28
        ' for note 24 only
        Decay3_time = value << ADSR_shift
        Case Rel3 '29
        ' for note 24 only
        Release3_Time = value << Release_Shift 'ADSR_shift
        Case 66
        'on/off for the robot
        If value = 0 Then ' power down
        GoSub PowerDown ' should reset controllers
        Set mute ' mutes the amps
        Else
        Clear mute
        Set poweron_led ' ok - yellow LED
        EndIf
        Case Sus1 '70
        ' sustain level for note1 22
        Sustain1_level = value
        ' if we want to allow modulation during the sounding of a note,
        ' we have to proceed as follows:
        If IEC0bits_T1IE = 1 Then ' tone generator works
        If ADSR1_flags = 0 Then ' we must be in the sustain phase!
        PDC1 = Ont[value]
        EndIf
        EndIf
        Case sus2 '71
        Sustain2_level = value
        If IEC1bits_T4IE = 1 Then ' if the note is sounding
        If ADSR2_flags = 0 Then ' if we are in the sustain phase
        PDC2 = Ont[value]
        EndIf
        EndIf
        Case Sus3 '72
        Sustain3_level = value
        If IEC1bits_T5IE = 1 Then ' if note3 sounds (irq enabled)
        If ADSR3_flags = 0 Then
        PDC3 = Ont[value]
        EndIf
        EndIf
        Case 123
        ' all notes off - no controller resets
        Clear PDC1
        Clear PDC2
        Clear PDC3
        Clear Note_Port1
        Clear Note_Port2
        Clear Note_Port3
        Clear ADSR1_flags
        Clear ADSR2_flags
        Clear ADSR3_flags
        Clear IEC0bits_T1IE ' disable the Timer1 interrupt
        Clear IEC1bits_T4IE ' disable timer4
        Clear IEC1bits_T5IE ' disable timer5
        Set resort_flag
        For i = 0 To NrTasks -1
        Set TimVals[i] ' stop timers
        Next i
    EndSelect
    Set Ctrl 'mandatory reset
Return

PowerDown:
        Set resort_flag
        For i = 0 To NrTasks -1
        Set TimVals[i]
        Next i
        Clear PDC1
        Clear PDC2
        Clear PDC3
        Set mute
        Clear poweron_led
        Low Note_Port1
        Low Note_Port2
        Low Note_Port3
        Clear ADSR1_flags
        Clear ADSR2_flags
        Clear ADSR3_flags
        Clear IEC0bits_T1IE ' disable the Timer1 interrupt
        Clear IEC1bits_T4IE ' disable Timer4 irq
        Clear IEC1bits_T5IE ' disable Timer5 irq
        GoSub Controller_Init_Prog0 ' set the defaults
Return

Controller_Init_Prog0:
        ' reset controllers to default start-up values:
      Attack1_time = 8 << ADSR_shift ' should be ca. 32ms . 64=250ms
      'Attack1_level = 127 'does not require an init, controlled by velo byte
      Decay1_time = 6 << ADSR_shift ' should be ca. ...
      Sustain1_level = 86 ' set with CC7
      Release1_Time = 10 << Release_Shift 'ADSR_shift ' set with release byte or ctrl
      bdutcy1 = 128 ' 50% duty cycle

      Attack2_time = 8 << ADSR_shift
      Decay2_time = 6 << ADSR_shift
      Sustain2_level = 86
      Release2_Time = 10 << Release_Shift 'ADSR_shift
      bdutcy2 = 128

      Attack3_time = 8 << ADSR_shift
      Decay3_time = 6 << ADSR_shift
      Sustain3_level = 86
      Release3_Time = 10 << Release_Shift 'ADSR_shift
      bdutcy3 = 128
      Clear C1val ' reset ctrl#1 (0-1024)
Return

Preset1:
      ' should give pizz
      Attack1_time = 2 << ADSR_shift
      Decay1_time = 0 ' should be ca. ...
      Sustain1_level = 28 '48 '86 ' set with CC7
      Release1_Time = 30 << Release_Shift 'ADSR_shift ' set with release byte or ctrl
      bdutcy1 = 11 'dutcy1 = 0.086

      Attack2_time = 2 << ADSR_shift
      Decay2_time = 0
      Sustain2_level = 28 '48
      Release2_Time = 30 << Release_Shift 'ADSR_shift
      bdutcy2 = 11 'dutcy2 = 0.086

      Attack3_time = 2 << ADSR_shift
      Decay3_time = 0
      Sustain3_level = 28 '48
      Release3_Time = 30 << Release_Shift 'ADSR_shift
      bdutcy3 = 11 'dutcy3 = 0.086
      C1val = 100 ' a bit rough! - ca. 10% jitter
Return

Preset2:
      ' should give nasal sound with slow attack
      Attack1_time = 25 << ADSR_shift
      Decay1_time = 10 << ADSR_shift
      Sustain1_level = 120 ' set with CC7
      Release1_Time = 50 << Release_Shift 'ADSR_shift' set with release byte or ctrl
      bdutcy1 = 3 'dutcy1 = 0.018

      Attack2_time = 25 << ADSR_shift
      Decay2_time = 10 << ADSR_shift
      Sustain2_level = 120
      Release2_Time = 50 << Release_Shift 'ADSR_shift
      bdutcy2 = 3 'dutcy2 = 0.018

      Attack3_time = 25 << ADSR_shift
      Decay3_time = 10 << ADSR_shift
      Sustain3_level = 120
      Release3_Time = 50 << Release_Shift 'ADSR_shift
      bdutcy3 = 3 'dutcy3 = 0.018
      C1val = 150 ' 15% jitter
Return

Preset3:
      ' round organ register
      Attack1_time = 8 << ADSR_shift
      Decay1_time = 2 << ADSR_shift
      Sustain1_level = 100 ' set with CC7
      Release1_Time = 10 << Release_Shift 'ADSR_shift ' set with release byte or ctrl
      bdutcy1 = 80 '47 'dutcy1 = 0.37

      Attack2_time = 8 << ADSR_shift
      Decay2_time = 2 << ADSR_shift
      Sustain2_level = 100
      Release2_Time = 10 << Release_Shift 'ADSR_shift
      bdutcy2 = 80 '47 'dutcy2 = 0.37

      Attack3_time = 8 << ADSR_shift
      Decay3_time = 2 << ADSR_shift
      Sustain3_level = 100
      Release3_Time = 10 << Release_Shift 'ADSR_shift
      bdutcy3 = 80 '47 'dutcy3 = 0.37
      C1val = 10 ' small jitter (= midi value 1)
Return

Preset4:
      ' should short sharp sound
      Attack1_time = 0
      Decay1_time = 0 ' should be ca. ...
      Sustain1_level = 127 ' set with CC7
      Release1_Time = 20 << Release_Shift 'ADSR_shift ' set with release byte or ctrl
      bdutcy1 = 3 'dutcy1 = 0.012

      Attack2_time = 0
      Decay2_time = 0
      Sustain2_level = 127
      Release2_Time = 20 << Release_Shift 'ADSR_shift
      bdutcy2 = 3 'dutcy2 = 0.012

      Attack3_time = 0
      Decay3_time = 0
      Sustain3_level = 127
      Release3_Time = 20 << Release_Shift 'ADSR_shift
      bdutcy3 = 3 'dutcy3 = 0.012
      C1val = 500 ' midi value = 63
Return

Preset5:
      ' to do
Return

Preset6:
      ' to do
Return

Preset7:
      ' to do
Return

Dur_Lookup:
'lookup for experiment. 1 dur unit is now 2.3us with loopcounter
'using timer23, 1 dur unit is 4.224 us
Set Dur[0]
Dur[1]= 23674 ' 03.08.2016: 56ms
        ' 04.08/2016: 66.2ms - 7.55 Hz
        ' 07.08.2016: 2x100ms = 200ms full period --> 5Hz [o.k.14.08.2016]
Dur[2]= 22917 ' freq= 2.18178644674259
Dur[3]= 22548 ' freq= 2.21749157353202
Dur[4]= 22185 ' freq= 2.25377507324769
Dur[5]= 21827 ' freq= 2.29074082558299
Dur[6]= 21475 ' freq= 2.32828870779977
Dur[7]= 21129 ' freq= 2.36641582658905
Dur[8]= 20789 ' freq= 2.40511809129828
Dur[9]= 20454 ' freq= 2.44450963136795
Dur[10]= 20124 ' freq= 2.48459550785132
Dur[11]= 19800 ' freq= 2.52525252525252
Dur[12]= 19481 ' freq= 2.56660335711719
Dur[13]= 19167 ' freq= 2.60865028434288
Dur[14]= 18858 ' freq= 2.65139463357726
Dur[15]= 18554 ' freq= 2.69483669289641
Dur[16]= 18255 ' freq= 2.73897562311695
Dur[17]= 17961 ' freq= 2.7838093647347
Dur[18]= 17672 ' freq= 2.82933454051607
Dur[19]= 17387 ' freq= 2.87571173865532
Dur[20]= 17107 ' freq= 2.92278014847723
Dur[21]= 16831 ' freq= 2.97070881112233
Dur[22]= 16560 ' freq= 3.01932367149758
Dur[23]= 16293 ' freq= 3.06880255324372
Dur[24]= 16030 ' freq= 3.11915159076731
Dur[25]= 15772 ' freq= 3.17017499365965
Dur[26]= 15518 ' freq= 3.22206469905916
Dur[27]= 15268 ' freq= 3.27482315954938
Dur[28]= 15022 ' freq= 3.32845160431367
Dur[29]= 14780 ' freq= 3.382949932341
Dur[30]= 14542 ' freq= 3.43831660019254
Dur[31]= 14307 ' freq= 3.4947927587894
Dur[32]= 14077 ' freq= 3.55189315905378
Dur[33]= 13850 ' freq= 3.6101083032491
Dur[34]= 13627 ' freq= 3.66918617450649
Dur[35]= 13407 ' freq= 3.72939509211606
Dur[36]= 13191 ' freq= 3.79046319460238
Dur[37]= 12978 ' freq= 3.85267375558638
Dur[38]= 12769 ' freq= 3.91573341686898
Dur[39]= 12564 ' freq= 3.97962432346386
Dur[40]= 12361 ' freq= 4.04498017959712
Dur[41]= 12162 ' freq= 4.1111659266568
Dur[42]= 11966 ' freq= 4.17850576633796
Dur[43]= 11773 ' freq= 4.24700586086809
Dur[44]= 11583 ' 07.08.2016: geeft 10.1177 Hz
Dur[45]= 11397 ' freq= 4.38711941739054
Dur[46]= 11213 ' freq= 4.45910996165165
Dur[47]= 11032 ' freq= 4.53226976069616
Dur[48]= 10855 ' freq= 4.60617227084293
Dur[49]= 10680 ' freq= 4.6816479400749
Dur[50]= 10508 ' freq= 4.75827940616673
Dur[51]= 10338 ' freq= 4.83652544012381
Dur[52]= 10172 ' freq= 4.91545418796697
Dur[53]= 10008 ' freq= 4.99600319744204
Dur[54]= 9846 ' freq= 5.07820434694292
Dur[55]= 9688 ' freq= 5.16102394715111
Dur[56]= 9532 ' freq= 5.24548887956357
Dur[57]= 9378 ' freq= 5.33162721262529
Dur[58]= 9227 ' freq= 5.4188793757451
Dur[59]= 9078 ' freq= 5.50782110597048
Dur[60]= 8932 ' freq= 5.59785042543663
Dur[61]= 8788 ' freq= 5.68957669549385
Dur[62]= 8646 ' freq= 5.78302105019662
Dur[63]= 8507 ' 04.08.2016: 21Hz pulse duur = 23.8ms
Dur[64]= 8370 ' geeft nu 20ms pulsen freq= 25Hz 03.08.2016
        ' 14.0017Hz 07.08.2016
Dur[65]= 8235 ' freq= 6.07164541590771
Dur[66]= 8102 ' freq= 6.17131572451246
Dur[67]= 7972 ' freq= 6.27195183140993
Dur[68]= 7843 ' freq= 6.37511156445238
Dur[69]= 7717 ' freq= 6.47920176234288
Dur[70]= 7593 ' freq= 6.58501251152377
Dur[71]= 7470 ' freq= 6.69344042838019
Dur[72]= 7350 ' freq= 6.80272108843537
Dur[73]= 7231 ' freq= 6.91467293597013
Dur[74]= 7115 ' freq= 7.02740688685875
Dur[75]= 7000 ' freq= 7.14285714285714
Dur[76]= 6888 ' freq= 7.25900116144018
Dur[77]= 6777 ' freq= 7.37789582411096
Dur[78]= 6667 ' freq= 7.49962501874906
Dur[79]= 6560 ' freq= 7.62195121951219
Dur[80]= 6454 ' freq= 7.74713356058258
Dur[81]= 6350 ' freq= 7.8740157480315
Dur[82]= 6248 ' freq= 8.00256081946223
Dur[83]= 6147 ' freq= 8.13404912965674
Dur[84]= 6048 ' freq= 8.26719576719577
Dur[85]= 5951 ' freq= 8.40194925222652
Dur[86]= 5855 ' freq= 8.5397096498719
Dur[87]= 5760 ' freq= 8.68055555555555
Dur[88]= 5668 ' freq= 8.82145377558222
Dur[89]= 5576 ' freq= 8.96700143472023
Dur[90]= 5486 ' freq= 9.11410864017499
Dur[91]= 5398 ' freq= 9.26268988514264
Dur[92]= 5311 ' freq= 9.41442289587648
Dur[93]= 5225 ' freq= 9.56937799043062
Dur[94]= 5141 ' freq= 9.72573429293912
Dur[95]= 5058 ' freq= 9.88533017002768
Dur[96]= 4977 ' freq= 10.0462125778581
Dur[97]= 4897 ' freq= 10.2103328568511
Dur[98]= 4818 ' freq= 10.3777501037775
Dur[99]= 4740 ' freq= 10.548523206751
Dur[100]= 4664 ' freq= 10.7204116638079
Dur[101]= 4589 ' freq= 10.8956199607758
Dur[102]= 4515 ' freq= 11.0741971207087
Dur[103]= 4442 ' freq= 11.2561909049977
Dur[104]= 4370 ' freq= 11.441647597254
Dur[105]= 4300 ' freq= 11.6279069767442
Dur[106]= 4231 ' freq= 11.8175372252422
Dur[107]= 4162 ' freq= 12.013455069678
Dur[108]= 4095 ' freq= 12.2100122100122
Dur[109]= 4029 ' freq= 12.4100273020601
Dur[110]= 3964 ' freq= 12.6135216952573
Dur[111]= 3901 ' freq= 12.8172263522174
Dur[112]= 3838 ' freq= 13.0276185513288
Dur[113]= 3776 ' freq= 13.2415254237288
Dur[114]= 3715 ' freq= 13.4589502018842
Dur[115]= 3655 ' freq= 13.6798905608755
Dur[116]= 3596 ' freq= 13.9043381535039
Dur[117]= 3538 ' freq= 14.1322781232335
Dur[118]= 3481 ' freq= 14.3636885952312
Dur[119]= 3425 ' freq= 14.5985401459854
Dur[120]= 3370 ' freq= 14.8367952522255
Dur[121]= 3316 ' freq= 15.0784077201448
Dur[122]= 3262 ' freq= 15.3280196198651
Dur[123]= 3210 ' freq= 15.5763239875389
Dur[124]= 3158 ' freq= 15.8328055731476
Dur[125]= 3107 ' freq= 16.0926939169617
Dur[126]= 3057 ' freq= 16.3559044815178 = 38.3365Hz 07.08.2016
Dur[127]= 3008 ' 03.08.2016: 6.9ms nu = 144Hz
        ' 04.08.2016: 8.35ms - 59.5Hz

Set Dur5[0] ' not used
Dur5[1]= 41667 ' freq= .999992000063999
Dur5[2]= 39494 ' freq= 1.0550125757499
Dur5[3]= 38450 ' freq= 1.08365843086259
Dur5[4]= 37434 ' freq= 1.11307011451265
Dur5[5]= 36445 ' freq= 1.14327525495038
Dur5[6]= 35482 ' freq= 1.17430434210774
Dur5[7]= 34544 ' freq= 1.20619113787247
Dur5[8]= 33631 ' freq= 1.23893629885126
Dur5[9]= 32743 ' freq= 1.27253662360403
Dur5[10]= 31877 ' freq= 1.30710752789367
Dur5[11]= 31035 ' freq= 1.34257021642232
Dur5[12]= 30215 ' freq= 1.37900601246621
Dur5[13]= 29416 ' freq= 1.41646269603844
Dur5[14]= 28639 ' freq= 1.45489251254117
Dur5[15]= 27882 ' freq= 1.49439303732396
Dur5[16]= 27146 ' freq= 1.53490999287802
Dur5[17]= 26428 ' freq= 1.57661066545583
Dur5[18]= 25730 ' freq= 1.61938074880166
Dur5[19]= 25050 ' freq= 1.66333998669328
Dur5[20]= 24388 ' freq= 1.70849051446066
Dur5[21]= 23743 ' freq= 1.75490319953951
Dur5[22]= 23116 ' freq= 1.8025033166061
Dur5[23]= 22505 ' freq= 1.85144042064726
Dur5[24]= 21910 ' freq= 1.90171915411532
Dur5[25]= 21331 ' freq= 1.95333864641445
Dur5[26]= 20768 ' freq= 2.006291730868
Dur5[27]= 20219 ' freq= 2.06076792455941
Dur5[28]= 19685 ' freq= 2.11667090000847
Dur5[29]= 19164 ' freq= 2.17421554303207
Dur5[30]= 18658 ' freq= 2.23317969057062
Dur5[31]= 18165 ' freq= 2.29378842095605
Dur5[32]= 17685 ' freq= 2.35604561304307
Dur5[33]= 17218 ' freq= 2.41994811631239
Dur5[34]= 16763 ' freq= 2.48563304102289
Dur5[35]= 16320 ' freq= 2.5531045751634
Dur5[36]= 15888 ' freq= 2.62252433702585
Dur5[37]= 15469 ' freq= 2.69355916133342
Dur5[38]= 15060 ' freq= 2.76671093404161
Dur5[39]= 14662 ' freq= 2.84181330423316
Dur5[40]= 14274 ' freq= 2.91906029610948
Dur5[41]= 13897 ' freq= 2.99824902257082
Dur5[42]= 13530 ' freq= 3.07957625030796
Dur5[43]= 13172 ' freq= 3.16327563518575
Dur5[44]= 12824 ' freq= 3.24911624038262
Dur5[45]= 12485 ' freq= 3.33733813910025
Dur5[46]= 12155 ' freq= 3.42794460441519
Dur5[47]= 11834 ' freq= 3.52092839840009
Dur5[48]= 11522 ' freq= 3.61627032343922
Dur5[49]= 11217 ' freq= 3.71459986330272
Dur5[50]= 10921 ' freq= 3.81527943106553
Dur5[51]= 10632 ' freq= 3.91898670679709
Dur5[52]= 10351 ' freq= 4.02537597011561
Dur5[53]= 10078 ' freq= 4.13441820467024
Dur5[54]= 9811 ' freq= 4.24693371385859
Dur5[55]= 9552 ' freq= 4.36208821887214
Dur5[56]= 9300 ' freq= 4.48028673835125
Dur5[57]= 9054 ' freq= 4.60201752448273
Dur5[58]= 8815 ' freq= 4.72679145396105
Dur5[59]= 8582 ' freq= 4.85512312592247
Dur5[60]= 8355 ' freq= 4.9870337123479
Dur5[61]= 8134 ' freq= 5.12253094008688
Dur5[62]= 7919 ' freq= 5.26160710527423
Dur5[63]= 7710 ' freq= 5.40423692174665
Dur5[64]= 7506 ' freq= 5.5511146638245
Dur5[65]= 7308 ' freq= 5.70151432220398
Dur5[66]= 7115 ' freq= 5.85617240571562
Dur5[67]= 6927 ' freq= 6.01510995621
Dur5[68]= 6744 ' freq= 6.1783313562673
Dur5[69]= 6565 ' freq= 6.34678852500635
Dur5[70]= 6392 ' freq= 6.51856487275761
Dur5[71]= 6223 ' freq= 6.69559162247576
Dur5[72]= 6059 ' freq= 6.87682235792485
Dur5[73]= 5898 ' freq= 7.06454165253758
Dur5[74]= 5743 ' freq= 7.25520924023449
Dur5[75]= 5591 ' freq= 7.45245334764204
Dur5[76]= 5443 ' freq= 7.65509216730969
Dur5[77]= 5299 ' freq= 7.86311882745172
Dur5[78]= 5159 ' freq= 8.07650061381405
Dur5[79]= 5023 ' freq= 8.29517552591413
Dur5[80]= 4890 ' freq= 8.52079072937969
Dur5[81]= 4761 ' freq= 8.75166281593503
Dur5[82]= 4635 ' freq= 8.98957209636821
Dur5[83]= 4513 ' freq= 9.23258734027624
Dur5[84]= 4393 ' freq= 9.48478640261021
Dur5[85]= 4277 ' freq= 9.74203101862676
Dur5[86]= 4164 ' freq= 10.0064040986231
Dur5[87]= 4054 ' freq= 10.277914816642
Dur5[88]= 3947 ' freq= 10.5565408326999
Dur5[89]= 3843 ' freq= 10.842223956978
Dur5[90]= 3741 ' freq= 11.1378419317473
Dur5[91]= 3642 ' freq= 11.4406004027091
Dur5[92]= 3546 ' freq= 11.7503290092122
Dur5[93]= 3452 ' freq= 12.0702974121282
Dur5[94]= 3361 ' freq= 12.3971040364971
Dur5[95]= 3272 ' freq= 12.7343113284434
Dur5[96]= 3186 ' freq= 13.0780498012136
Dur5[97]= 3102 ' freq= 13.4321942832581
Dur5[98]= 3020 ' freq= 13.7969094922737
Dur5[99]= 2940 ' freq= 14.172335600907
Dur5[100]= 2862 ' freq= 14.5585837409737
Dur5[101]= 2787 ' freq= 14.9503647889008
Dur5[102]= 2713 ' freq= 15.3581521071385
Dur5[103]= 2641 ' freq= 15.7768522024486
Dur5[104]= 2571 ' freq= 16.2064047711656
Dur5[105]= 2504 ' freq= 16.640042598509
Dur5[106]= 2437 ' freq= 17.0975242784845
Dur5[107]= 2373 ' freq= 17.5586458772299
Dur5[108]= 2310 ' freq= 18.037518037518
Dur5[109]= 2249 ' freq= 18.5267526307989
Dur5[110]= 2190 ' freq= 19.0258751902588
Dur5[111]= 2132 ' freq= 19.5434646654159
Dur5[112]= 2076 ' freq= 20.0706486833654
Dur5[113]= 2021 ' freq= 20.616856341745
Dur5[114]= 1967 ' freq= 21.182850364345
Dur5[115]= 1915 ' freq= 21.7580504786771
Dur5[116]= 1865 ' freq= 22.3413762287757
Dur5[117]= 1815 ' freq= 22.9568411386593
Dur5[118]= 1767 ' freq= 23.5804565176382
Dur5[119]= 1721 ' freq= 24.2107301956227
Dur5[120]= 1675 ' freq= 24.8756218905473
Dur5[121]= 1631 ' freq= 25.5466993664418
Dur5[122]= 1588 ' freq= 26.2384550797649
Dur5[123]= 1546 ' freq= 26.9512721000431
Dur5[124]= 1505 ' freq= 27.6854928017719
Dur5[125]= 1465 ' freq= 28.4414106939704
Dur5[126]= 1427 ' freq= 29.1987853305302
Dur5[127]= 1389 ' freq= 29.9976001919846
For i = 0 To 127
    Dur5[i] = Dur5[i] >> 3 'so range becomes 8Hz to 240Hz
Next i
Return

' midi-note to period lookup for PIC24 with 120MHz clock
' time_unit = 8.33333333333333E-9
' divider set to = 64
' lowest note = midi 22 (Sib) , freq = 29.1355235 Hz

Period_Lookup_Table:
Period[22]= 64355 ' soll frequency = 29.13523 real frequency = 29.13526
Period[23]= 60743 ' soll frequency = 30.86771 real frequency = 30.86775
Period[24]= 57334 ' soll frequency = 32.70319 real frequency = 32.70311
Period[25]= 54116 ' soll frequency = 34.64783 real frequency = 34.64779
Period[26]= 51079 ' soll frequency = 36.7081 real frequency = 36.70784
Period[27]= 48212 ' soll frequency = 38.89087 real frequency = 38.89073
Period[28]= 45506 ' soll frequency = 41.20344 real frequency = 41.20336
Period[29]= 42952 ' soll frequency = 43.65353 real frequency = 43.65338
Period[30]= 40541 ' soll frequency = 46.2493 real frequency = 46.24948
Period[31]= 38266 ' soll frequency = 48.99943 real frequency = 48.99911
Period[32]= 36118 ' soll frequency = 51.91308 real frequency = 51.91317
Period[33]= 34091 ' soll frequency = 55 real frequency = 54.99986
Period[34]= 32178 ' soll frequency = 58.27047 real frequency = 58.26963
Period[35]= 30372 ' soll frequency = 61.73541 real frequency = 61.73449
Period[36]= 28667 ' soll frequency = 65.40639 real frequency = 65.40622
Period[37]= 27058 ' soll frequency = 69.29565 real frequency = 69.29558
Period[38]= 25539 ' soll frequency = 73.41619 real frequency = 73.41713
Period[39]= 24106 ' soll frequency = 77.78174 real frequency = 77.78146
Period[40]= 22753 ' soll frequency = 82.40689 real frequency = 82.40672
Period[41]= 21476 ' soll frequency = 87.30706 real frequency = 87.30676
Period[42]= 20271 ' soll frequency = 92.4986 real frequency = 92.49667
Period[43]= 19133 ' soll frequency = 97.99886 real frequency = 97.99822
Period[44]= 18059 ' soll frequency = 103.8262 real frequency = 103.8263
Period[45]= 17045 ' soll frequency = 110 real frequency = 110.0029
Period[46]= 16089 ' soll frequency = 116.5409 real frequency = 116.5392
Period[47]= 15186 ' soll frequency = 123.4708 real frequency = 123.469
Period[48]= 14333 ' soll frequency = 130.8128 real frequency = 130.817
Period[49]= 13529 ' soll frequency = 138.5913 real frequency = 138.5912
Period[50]= 12770 ' soll frequency = 146.8324 real frequency = 146.8285
Period[51]= 12053 ' soll frequency = 155.5635 real frequency = 155.5629
Period[52]= 11376 ' soll frequency = 164.8138 real frequency = 164.8207
Period[53]= 10738 ' soll frequency = 174.6141 real frequency = 174.6135
Period[54]= 10135 ' soll frequency = 184.9972 real frequency = 185.0025
Period[55]= 9566 ' soll frequency = 195.9977 real frequency = 196.0067
Period[56]= 9030 ' soll frequency = 207.6523 real frequency = 207.6412
Period[57]= 8523 ' soll frequency = 220 real frequency = 219.993
Period[58]= 8044 ' soll frequency = 233.0819 real frequency = 233.093
Period[59]= 7593 ' soll frequency = 246.9416 real frequency = 246.938
Period[60]= 7167 ' soll frequency = 261.6255 real frequency = 261.6158
Period[61]= 6764 ' soll frequency = 277.1826 real frequency = 277.2028
Period[62]= 6385 ' soll frequency = 293.6648 real frequency = 293.657
Period[63]= 6026 ' soll frequency = 311.127 real frequency = 311.1517
Period[64]= 5688 ' soll frequency = 329.6276 real frequency = 329.6414
Period[65]= 5369 ' soll frequency = 349.2282 real frequency = 349.227
Period[66]= 5068 ' soll frequency = 369.9944 real frequency = 369.9684
Period[67]= 4783 ' soll frequency = 391.9954 real frequency = 392.0134
Period[68]= 4515 ' soll frequency = 415.3047 real frequency = 415.2824
Period[69]= 4261 ' soll frequency = 440 real frequency = 440.0375
Period[70]= 4022 ' soll frequency = 466.1638 real frequency = 466.186
Period[71]= 3796 ' soll frequency = 493.8833 real frequency = 493.941
Period[72]= 3583 ' soll frequency = 523.2511 real frequency = 523.3045
Period[73]= 3382 ' soll frequency = 554.3652 real frequency = 554.4057
Period[74]= 3192 ' soll frequency = 587.3295 real frequency = 587.406
Period[75]= 3013 ' soll frequency = 622.254 real frequency = 622.3033
Period[76]= 2844 ' soll frequency = 659.2551 real frequency = 659.2827
Period[77]= 2684 ' soll frequency = 698.4565 real frequency = 698.5842
Period[78]= 2534 ' soll frequency = 739.9888 real frequency = 739.9368
Period[79]= 2392 ' soll frequency = 783.9908 real frequency = 783.8628
Period[80]= 2257 ' soll frequency = 830.6094 real frequency = 830.7488
Period[81]= 2131 ' soll frequency = 880 real frequency = 879.8686
Period[82]= 2011 ' soll frequency = 932.3275 real frequency = 932.3719
Period[83]= 1898 ' soll frequency = 987.7666 real frequency = 987.882
Period[84]= 1792 ' soll frequency = 1046.502 real frequency = 1046.317
Period[85]= 1691 ' soll frequency = 1108.73 real frequency = 1108.811
Period[86]= 1596 ' soll frequency = 1174.659 real frequency = 1174.812
Period[87]= 1507 ' soll frequency = 1244.508 real frequency = 1244.194
Period[88]= 1422 ' soll frequency = 1318.51 real frequency = 1318.565
Period[89]= 1342 ' soll frequency = 1396.913 real frequency = 1397.168
Period[90]= 1267 ' soll frequency = 1479.978 real frequency = 1479.874
Period[91]= 1196 ' soll frequency = 1567.982 real frequency = 1567.726
Period[92]= 1129 ' soll frequency = 1661.219 real frequency = 1660.762
Period[93]= 1065 ' soll frequency = 1760 real frequency = 1760.563
Period[94]= 1006 ' soll frequency = 1864.655 real frequency = 1863.817
Period[95]= 949 ' soll frequency = 1975.533 real frequency = 1975.764
Period[96]= 896 ' soll frequency = 2093.004 real frequency = 2092.634
Period[97]= 846 ' soll frequency = 2217.461 real frequency = 2216.312
Period[98]= 798 ' soll frequency = 2349.318 real frequency = 2349.624
Period[99]= 753 ' soll frequency = 2489.016 real frequency = 2490.04
Period[100]= 711 ' soll frequency = 2637.02 real frequency = 2637.131
Period[101]= 671 ' soll frequency = 2793.826 real frequency = 2794.337
Period[102]= 633 ' soll frequency = 2959.955 real frequency = 2962.085
Period[103]= 598 ' soll frequency = 3135.963 real frequency = 3135.451
Period[104]= 564 ' soll frequency = 3322.438 real frequency = 3324.468
Period[105]= 533 ' soll frequency = 3520 real frequency = 3517.824
Period[106]= 503 ' soll frequency = 3729.31 real frequency = 3727.634
Period[107]= 475 ' soll frequency = 3951.066 real frequency = 3947.368
Period[108]= 448 ' soll frequency = 4186.009 real frequency = 4185.268
Period[109]= 423 ' soll frequency = 4434.922 real frequency = 4432.624
Period[110]= 399 ' soll frequency = 4698.636 real frequency = 4699.248
Period[111]= 377 ' soll frequency = 4978.032 real frequency = 4973.475
Period[112]= 356 ' soll frequency = 5274.041 real frequency = 5266.854
Period[113]= 336 ' soll frequency = 5587.652 real frequency = 5580.357
Period[114]= 317 ' soll frequency = 5919.911 real frequency = 5914.827
Period[115]= 299 ' soll frequency = 6271.927 real frequency = 6270.903
Period[116]= 282 ' soll frequency = 6644.875 real frequency = 6648.936
Period[117]= 266 ' soll frequency = 7040 real frequency = 7048.872
Period[118]= 251 ' soll frequency = 7458.62 real frequency = 7470.12
Period[119]= 237 ' soll frequency = 7902.133 real frequency = 7911.392
Period[120]= 224 ' soll frequency = 8372.018 real frequency = 8370.536
Period[121]= 211 ' soll frequency = 8869.844 real frequency = 8886.256
Period[122]= 200 ' soll frequency = 9397.272 real frequency = 9375
Period[123]= 188 ' soll frequency = 9956.063 real frequency = 9973.404
Period[124]= 178 ' soll frequency = 10548.08 real frequency = 10533.71
Period[125]= 168 ' soll frequency = 11175.3 real frequency = 11160.71
Period[126]= 158 ' soll frequency = 11839.82 real frequency = 11867.09
Period[127]= 149 ' soll frequency = 12543.85 real frequency = 12583.89
Return

' pwm on/off values for PIC24 with 120MHz clock
' time_unit = 8.33333333333333E-9
' divider set to = 8
' using a 16 bit timers (timer1, 4, 5)
' PWM base frequency = 15000
' with divider set to 1 pwm base freq becomes 120kHz
' so with the 16-bit values below we would get an audible 915Hz pitch...
' divider set to 1 does not work, it freezes the PIC,
' so we must use :8
' Note 09.10.2016: 60dB range is exagerated.
' would be better with a 40dB or even 34dB range.
' PWM base frequency can be halved as well...

PWM_Lookup_Table_60dB_Versie1:
Ont[0]= 64 : Oft[0]= 63936 ' db= -60
Ont[1]= 68 : Oft[1]= 63932 ' db= -59
Ont[2]= 71 : Oft[2]= 63929 ' db= -59
Ont[3]= 75 : Oft[3]= 63925 ' db= -59
Ont[4]= 80 : Oft[4]= 63920 ' db= -58
Ont[5]= 84 : Oft[5]= 63916 ' db= -58
Ont[6]= 89 : Oft[6]= 63911 ' db= -57
Ont[7]= 94 : Oft[7]= 63906 ' db= -57
Ont[8]= 99 : Oft[8]= 63901 ' db= -56
Ont[9]= 104 : Oft[9]= 63896 ' db= -56
Ont[10]= 110 : Oft[10]= 63890 ' db= -55
Ont[11]= 116 : Oft[11]= 63884 ' db= -55
Ont[12]= 123 : Oft[12]= 63877 ' db= -54
Ont[13]= 130 : Oft[13]= 63870 ' db= -54
Ont[14]= 137 : Oft[14]= 63863 ' db= -53
Ont[15]= 145 : Oft[15]= 63855 ' db= -53
Ont[16]= 153 : Oft[16]= 63847 ' db= -52
Ont[17]= 161 : Oft[17]= 63839 ' db= -52
Ont[18]= 170 : Oft[18]= 63830 ' db= -52
Ont[19]= 180 : Oft[19]= 63820 ' db= -51
Ont[20]= 190 : Oft[20]= 63810 ' db= -51
Ont[21]= 201 : Oft[21]= 63799 ' db= -50
Ont[22]= 212 : Oft[22]= 63788 ' db= -50
Ont[23]= 224 : Oft[23]= 63776 ' db= -49
Ont[24]= 236 : Oft[24]= 63764 ' db= -49
Ont[25]= 249 : Oft[25]= 63751 ' db= -48
Ont[26]= 263 : Oft[26]= 63737 ' db= -48
Ont[27]= 278 : Oft[27]= 63722 ' db= -47
Ont[28]= 293 : Oft[28]= 63707 ' db= -47
Ont[29]= 310 : Oft[29]= 63690 ' db= -46
Ont[30]= 327 : Oft[30]= 63673 ' db= -46
Ont[31]= 346 : Oft[31]= 63654 ' db= -45
Ont[32]= 365 : Oft[32]= 63635 ' db= -45
Ont[33]= 385 : Oft[33]= 63615 ' db= -44
Ont[34]= 407 : Oft[34]= 63593 ' db= -44
Ont[35]= 429 : Oft[35]= 63571 ' db= -43
Ont[36]= 453 : Oft[36]= 63547 ' db= -43
Ont[37]= 479 : Oft[37]= 63521 ' db= -43
Ont[38]= 506 : Oft[38]= 63494 ' db= -42
Ont[39]= 534 : Oft[39]= 63466 ' db= -42
Ont[40]= 564 : Oft[40]= 63436 ' db= -41
Ont[41]= 595 : Oft[41]= 63405 ' db= -41
Ont[42]= 629 : Oft[42]= 63371 ' db= -40
Ont[43]= 664 : Oft[43]= 63336 ' db= -40
Ont[44]= 701 : Oft[44]= 63299 ' db= -39
Ont[45]= 740 : Oft[45]= 63260 ' db= -39
Ont[46]= 781 : Oft[46]= 63219 ' db= -38
Ont[47]= 825 : Oft[47]= 63175 ' db= -38
Ont[48]= 871 : Oft[48]= 63129 ' db= -37
Ont[49]= 920 : Oft[49]= 63080 ' db= -37
Ont[50]= 971 : Oft[50]= 63029 ' db= -36
Ont[51]= 1025 : Oft[51]= 62975 ' db= -36
Ont[52]= 1083 : Oft[52]= 62917 ' db= -35
Ont[53]= 1143 : Oft[53]= 62857 ' db= -35
Ont[54]= 1207 : Oft[54]= 62793 ' db= -34
Ont[55]= 1275 : Oft[55]= 62725 ' db= -34
Ont[56]= 1346 : Oft[56]= 62654 ' db= -34
Ont[57]= 1421 : Oft[57]= 62579 ' db= -33
Ont[58]= 1501 : Oft[58]= 62499 ' db= -33
Ont[59]= 1584 : Oft[59]= 62416 ' db= -32
Ont[60]= 1673 : Oft[60]= 62327 ' db= -32
Ont[61]= 1767 : Oft[61]= 62233 ' db= -31
Ont[62]= 1865 : Oft[62]= 62135 ' db= -31
Ont[63]= 1970 : Oft[63]= 62030 ' db= -30
Ont[64]= 2080 : Oft[64]= 61920 ' db= -30
Ont[65]= 2196 : Oft[65]= 61804 ' db= -29
Ont[66]= 2319 : Oft[66]= 61681 ' db= -29
Ont[67]= 2448 : Oft[67]= 61552 ' db= -28
Ont[68]= 2585 : Oft[68]= 61415 ' db= -28
Ont[69]= 2730 : Oft[69]= 61270 ' db= -27
Ont[70]= 2882 : Oft[70]= 61118 ' db= -27
Ont[71]= 3043 : Oft[71]= 60957 ' db= -26
Ont[72]= 3213 : Oft[72]= 60787 ' db= -26
Ont[73]= 3393 : Oft[73]= 60607 ' db= -26
Ont[74]= 3583 : Oft[74]= 60417 ' db= -25
Ont[75]= 3783 : Oft[75]= 60217 ' db= -25
Ont[76]= 3994 : Oft[76]= 60006 ' db= -24
Ont[77]= 4218 : Oft[77]= 59782 ' db= -24
Ont[78]= 4453 : Oft[78]= 59547 ' db= -23
Ont[79]= 4702 : Oft[79]= 59298 ' db= -23
Ont[80]= 4965 : Oft[80]= 59035 ' db= -22
Ont[81]= 5243 : Oft[81]= 58757 ' db= -22
Ont[82]= 5536 : Oft[82]= 58464 ' db= -21
Ont[83]= 5845 : Oft[83]= 58155 ' db= -21
Ont[84]= 6172 : Oft[84]= 57828 ' db= -20
Ont[85]= 6517 : Oft[85]= 57483 ' db= -20
Ont[86]= 6881 : Oft[86]= 57119 ' db= -19
Ont[87]= 7266 : Oft[87]= 56734 ' db= -19
Ont[88]= 7672 : Oft[88]= 56328 ' db= -18
Ont[89]= 8101 : Oft[89]= 55899 ' db= -18
Ont[90]= 8554 : Oft[90]= 55446 ' db= -17
Ont[91]= 9032 : Oft[91]= 54968 ' db= -17
Ont[92]= 9537 : Oft[92]= 54463 ' db= -17
Ont[93]= 10070 : Oft[93]= 53930 ' db= -16
Ont[94]= 10633 : Oft[94]= 53367 ' db= -16
Ont[95]= 11227 : Oft[95]= 52773 ' db= -15
Ont[96]= 11855 : Oft[96]= 52145 ' db= -15
Ont[97]= 12518 : Oft[97]= 51482 ' db= -14
Ont[98]= 13217 : Oft[98]= 50783 ' db= -14
Ont[99]= 13956 : Oft[99]= 50044 ' db= -13
Ont[100]= 14736 : Oft[100]= 49264 ' db= -13
Ont[101]= 15560 : Oft[101]= 48440 ' db= -12
Ont[102]= 16430 : Oft[102]= 47570 ' db= -12
Ont[103]= 17348 : Oft[103]= 46652 ' db= -11
Ont[104]= 18318 : Oft[104]= 45682 ' db= -11
Ont[105]= 19342 : Oft[105]= 44658 ' db= -10
Ont[106]= 20423 : Oft[106]= 43577 ' db= -10
Ont[107]= 21564 : Oft[107]= 42436 ' db= -9
Ont[108]= 22770 : Oft[108]= 41230 ' db= -9
Ont[109]= 24043 : Oft[109]= 39957 ' db= -9
Ont[110]= 25387 : Oft[110]= 38613 ' db= -8
Ont[111]= 26806 : Oft[111]= 37194 ' db= -8
Ont[112]= 28304 : Oft[112]= 35696 ' db= -7
Ont[113]= 29886 : Oft[113]= 34114 ' db= -7
Ont[114]= 31557 : Oft[114]= 32443 ' db= -6
Ont[115]= 33321 : Oft[115]= 30679 ' db= -6
Ont[116]= 35183 : Oft[116]= 28817 ' db= -5
Ont[117]= 37150 : Oft[117]= 26850 ' db= -5
Ont[118]= 39227 : Oft[118]= 24773 ' db= -4
Ont[119]= 41419 : Oft[119]= 22581 ' db= -4
Ont[120]= 43735 : Oft[120]= 20265 ' db= -3
Ont[121]= 46179 : Oft[121]= 17821 ' db= -3
Ont[122]= 48761 : Oft[122]= 15239 ' db= -2
Ont[123]= 51486 : Oft[123]= 12514 ' db= -2
Ont[124]= 54364 : Oft[124]= 9636 ' db= -1
Ont[125]= 57403 : Oft[125]= 6597 ' db= -1
Ont[126]= 60612 : Oft[126]= 3388 ' db= 0
Ont[127]= 64000 : Oft[127]= 64 ' db= 0
' following just reduces the number of steps in the timer loop for the ADSR
For i = 0 To 127
    Ont[i] = Ont[i] >> 6 '5 ' geeft pwm freq = 126Hz nu
    Oft[i] = Oft[i] >> 6 '5 ' :64 :32
Next i

Return

' pwm on/off values for PIC24 with 120MHz clock
' time_unit = 8.33333333333333E-9
' divider set to = 8
' using a 32 bit timer (timer2+3)
' PWM base frequency = 117000Hz [measured 9.10.2016]
' Dynamic range = 40dB

PWM_Lookup_Table_40dB_Versie1:
   ' lookup with pwm values for PDC1,2,3
   ' resolution here is 13-bits
   ' dynamic range = 40dB (1:100)
   ' Deze lookup gebruikt niet de optimale uitsturing.
   ' De signaal ruisafstand kan beter...
Ont[0]= 64 : Oft[0]= 6336 ' db= -40
Ont[1]= 66 : Oft[1]= 6334 ' db= -40
Ont[2]= 69 : Oft[2]= 6331 ' db= -39
Ont[3]= 71 : Oft[3]= 6329 ' db= -39
Ont[4]= 74 : Oft[4]= 6326 ' db= -39
Ont[5]= 77 : Oft[5]= 6323 ' db= -38
Ont[6]= 80 : Oft[6]= 6320 ' db= -38
Ont[7]= 82 : Oft[7]= 6318 ' db= -38
Ont[8]= 86 : Oft[8]= 6314 ' db= -37
Ont[9]= 89 : Oft[9]= 6311 ' db= -37
Ont[10]= 92 : Oft[10]= 6308 ' db= -37
Ont[11]= 95 : Oft[11]= 6305 ' db= -37
Ont[12]= 99 : Oft[12]= 6301 ' db= -36
Ont[13]= 103 : Oft[13]= 6297 ' db= -36
Ont[14]= 106 : Oft[14]= 6294 ' db= -36
Ont[15]= 110 : Oft[15]= 6290 ' db= -35
Ont[16]= 114 : Oft[16]= 6286 ' db= -35
Ont[17]= 119 : Oft[17]= 6281 ' db= -35
Ont[18]= 123 : Oft[18]= 6277 ' db= -34
Ont[19]= 127 : Oft[19]= 6273 ' db= -34
Ont[20]= 132 : Oft[20]= 6268 ' db= -34
Ont[21]= 137 : Oft[21]= 6263 ' db= -33
Ont[22]= 142 : Oft[22]= 6258 ' db= -33
Ont[23]= 147 : Oft[23]= 6253 ' db= -33
Ont[24]= 153 : Oft[24]= 6247 ' db= -32
Ont[25]= 158 : Oft[25]= 6242 ' db= -32
Ont[26]= 164 : Oft[26]= 6236 ' db= -32
Ont[27]= 170 : Oft[27]= 6230 ' db= -32
Ont[28]= 177 : Oft[28]= 6223 ' db= -31
Ont[29]= 183 : Oft[29]= 6217 ' db= -31
Ont[30]= 190 : Oft[30]= 6210 ' db= -31
Ont[31]= 197 : Oft[31]= 6203 ' db= -30
Ont[32]= 204 : Oft[32]= 6196 ' db= -30
Ont[33]= 212 : Oft[33]= 6188 ' db= -30
Ont[34]= 220 : Oft[34]= 6180 ' db= -29
Ont[35]= 228 : Oft[35]= 6172 ' db= -29
Ont[36]= 236 : Oft[36]= 6164 ' db= -29
Ont[37]= 245 : Oft[37]= 6155 ' db= -28
Ont[38]= 254 : Oft[38]= 6146 ' db= -28
Ont[39]= 263 : Oft[39]= 6137 ' db= -28
Ont[40]= 273 : Oft[40]= 6127 ' db= -27
Ont[41]= 283 : Oft[41]= 6117 ' db= -27
Ont[42]= 293 : Oft[42]= 6107 ' db= -27
Ont[43]= 304 : Oft[43]= 6096 ' db= -26
Ont[44]= 316 : Oft[44]= 6084 ' db= -26
Ont[45]= 327 : Oft[45]= 6073 ' db= -26
Ont[46]= 339 : Oft[46]= 6061 ' db= -26
Ont[47]= 352 : Oft[47]= 6048 ' db= -25
Ont[48]= 365 : Oft[48]= 6035 ' db= -25
Ont[49]= 378 : Oft[49]= 6022 ' db= -25
Ont[50]= 392 : Oft[50]= 6008 ' db= -24
Ont[51]= 407 : Oft[51]= 5993 ' db= -24
Ont[52]= 422 : Oft[52]= 5978 ' db= -24
Ont[53]= 437 : Oft[53]= 5963 ' db= -23
Ont[54]= 453 : Oft[54]= 5947 ' db= -23
Ont[55]= 470 : Oft[55]= 5930 ' db= -23
Ont[56]= 488 : Oft[56]= 5912 ' db= -22
Ont[57]= 506 : Oft[57]= 5894 ' db= -22
Ont[58]= 524 : Oft[58]= 5876 ' db= -22
Ont[59]= 544 : Oft[59]= 5856 ' db= -21
Ont[60]= 564 : Oft[60]= 5836 ' db= -21
Ont[61]= 585 : Oft[61]= 5815 ' db= -21
Ont[62]= 606 : Oft[62]= 5794 ' db= -20
Ont[63]= 629 : Oft[63]= 5771 ' db= -20
Ont[64]= 652 : Oft[64]= 5748 ' db= -20
Ont[65]= 676 : Oft[65]= 5724 ' db= -20
Ont[66]= 701 : Oft[66]= 5699 ' db= -19
Ont[67]= 727 : Oft[67]= 5673 ' db= -19
Ont[68]= 753 : Oft[68]= 5647 ' db= -19
Ont[69]= 781 : Oft[69]= 5619 ' db= -18
Ont[70]= 810 : Oft[70]= 5590 ' db= -18
Ont[71]= 840 : Oft[71]= 5560 ' db= -18
Ont[72]= 871 : Oft[72]= 5529 ' db= -17
Ont[73]= 903 : Oft[73]= 5497 ' db= -17
Ont[74]= 937 : Oft[74]= 5463 ' db= -17
Ont[75]= 971 : Oft[75]= 5429 ' db= -16
Ont[76]= 1007 : Oft[76]= 5393 ' db= -16
Ont[77]= 1044 : Oft[77]= 5356 ' db= -16
Ont[78]= 1083 : Oft[78]= 5317 ' db= -15
Ont[79]= 1123 : Oft[79]= 5277 ' db= -15
Ont[80]= 1164 : Oft[80]= 5236 ' db= -15
Ont[81]= 1207 : Oft[81]= 5193 ' db= -14
Ont[82]= 1252 : Oft[82]= 5148 ' db= -14
Ont[83]= 1298 : Oft[83]= 5102 ' db= -14
Ont[84]= 1346 : Oft[84]= 5054 ' db= -14
Ont[85]= 1396 : Oft[85]= 5004 ' db= -13
Ont[86]= 1447 : Oft[86]= 4953 ' db= -13
Ont[87]= 1501 : Oft[87]= 4899 ' db= -13
Ont[88]= 1556 : Oft[88]= 4844 ' db= -12
Ont[89]= 1613 : Oft[89]= 4787 ' db= -12
Ont[90]= 1673 : Oft[90]= 4727 ' db= -12
Ont[91]= 1735 : Oft[91]= 4665 ' db= -11
Ont[92]= 1799 : Oft[92]= 4601 ' db= -11
Ont[93]= 1865 : Oft[93]= 4535 ' db= -11
Ont[94]= 1934 : Oft[94]= 4466 ' db= -10
Ont[95]= 2006 : Oft[95]= 4394 ' db= -10
Ont[96]= 2080 : Oft[96]= 4320 ' db= -10
Ont[97]= 2156 : Oft[97]= 4244 ' db= -9
Ont[98]= 2236 : Oft[98]= 4164 ' db= -9
Ont[99]= 2319 : Oft[99]= 4081 ' db= -9
Ont[100]= 2404 : Oft[100]= 3996 ' db= -9
Ont[101]= 2493 : Oft[101]= 3907 ' db= -8
Ont[102]= 2585 : Oft[102]= 3815 ' db= -8
Ont[103]= 2681 : Oft[103]= 3719 ' db= -8
Ont[104]= 2780 : Oft[104]= 3620 ' db= -7
Ont[105]= 2882 : Oft[105]= 3518 ' db= -7
Ont[106]= 2989 : Oft[106]= 3411 ' db= -7
Ont[107]= 3099 : Oft[107]= 3301 ' db= -6
Ont[108]= 3213 : Oft[108]= 3187 ' db= -6
Ont[109]= 3332 : Oft[109]= 3068 ' db= -6
Ont[110]= 3455 : Oft[110]= 2945 ' db= -5
Ont[111]= 3583 : Oft[111]= 2817 ' db= -5
Ont[112]= 3715 : Oft[112]= 2685 ' db= -5
Ont[113]= 3852 : Oft[113]= 2548 ' db= -4
Ont[114]= 3994 : Oft[114]= 2406 ' db= -4
Ont[115]= 4142 : Oft[115]= 2258 ' db= -4
Ont[116]= 4295 : Oft[116]= 2105 ' db= -3
Ont[117]= 4453 : Oft[117]= 1947 ' db= -3
Ont[118]= 4618 : Oft[118]= 1782 ' db= -3
Ont[119]= 4788 : Oft[119]= 1612 ' db= -3
Ont[120]= 4965 : Oft[120]= 1435 ' db= -2
Ont[121]= 5149 : Oft[121]= 1251 ' db= -2
Ont[122]= 5339 : Oft[122]= 1061 ' db= -2
Ont[123]= 5536 : Oft[123]= 864 ' db= -1
Ont[124]= 5740 : Oft[124]= 660 ' db= -1
Ont[125]= 5952 : Oft[125]= 448 ' db= -1
Ont[126]= 6172 : Oft[126]= 228 ' db= 0
Ont[127]= 6400 : Oft[127]= 0 ' db= 0
Return

PWM_Lookup_Table_40dB:
'HybrLo volume logscales 40dB
'for 16bit PWM values met volledige uitsturing
Ont[127]= 65535 ' db= 0
Ont[126]= 63220 ' db= 0
Ont[125]= 60986 ' db= -1
Ont[124]= 58831 ' db= -1
Ont[123]= 56752 ' db= -1
Ont[122]= 54746 ' db= -2
Ont[121]= 52812 ' db= -2
Ont[120]= 50945 ' db= -2
Ont[119]= 49145 ' db= -3
Ont[118]= 47408 ' db= -3
Ont[117]= 45733 ' db= -3
Ont[116]= 44117 ' db= -3
Ont[115]= 42558 ' db= -4
Ont[114]= 41054 ' db= -4
Ont[113]= 39603 ' db= -4
Ont[112]= 38204 ' db= -5
Ont[111]= 36854 ' db= -5
Ont[110]= 35551 ' db= -5
Ont[109]= 34295 ' db= -6
Ont[108]= 33083 ' db= -6
Ont[107]= 31914 ' db= -6
Ont[106]= 30786 ' db= -7
Ont[105]= 29698 ' db= -7
Ont[104]= 28649 ' db= -7
Ont[103]= 27636 ' db= -8
Ont[102]= 26660 ' db= -8
Ont[101]= 25718 ' db= -8
Ont[100]= 24809 ' db= -8
Ont[99]= 23932 ' db= -9
Ont[98]= 23086 ' db= -9
Ont[97]= 22270 ' db= -9
Ont[96]= 21483 ' db= -10
Ont[95]= 20724 ' db= -10
Ont[94]= 19992 ' db= -10
Ont[93]= 19285 ' db= -11
Ont[92]= 18604 ' db= -11
Ont[91]= 17947 ' db= -11
Ont[90]= 17312 ' db= -12
Ont[89]= 16701 ' db= -12
Ont[88]= 16110 ' db= -12
Ont[87]= 15541 ' db= -13
Ont[86]= 14992 ' db= -13
Ont[85]= 14462 ' db= -13
Ont[84]= 13951 ' db= -13
Ont[83]= 13458 ' db= -14
Ont[82]= 12982 ' db= -14
Ont[81]= 12524 ' db= -14
Ont[80]= 12081 ' db= -15
Ont[79]= 11654 ' db= -15
Ont[78]= 11242 ' db= -15
Ont[77]= 10845 ' db= -16
Ont[76]= 10462 ' db= -16
Ont[75]= 10092 ' db= -16
Ont[74]= 9735 ' db= -17
Ont[73]= 9391 ' db= -17
Ont[72]= 9060 ' db= -17
Ont[71]= 8739 ' db= -18
Ont[70]= 8431 ' db= -18
Ont[69]= 8133 ' db= -18
Ont[68]= 7845 ' db= -18
Ont[67]= 7568 ' db= -19
Ont[66]= 7301 ' db= -19
Ont[65]= 7043 ' db= -19
Ont[64]= 6794 ' db= -20
Ont[63]= 6554 ' db= -20
Ont[62]= 6322 ' db= -20
Ont[61]= 6099 ' db= -21
Ont[60]= 5883 ' db= -21
Ont[59]= 5675 ' db= -21
Ont[58]= 5475 ' db= -22
Ont[57]= 5281 ' db= -22
Ont[56]= 5095 ' db= -22
Ont[55]= 4915 ' db= -22
Ont[54]= 4741 ' db= -23
Ont[53]= 4573 ' db= -23
Ont[52]= 4412 ' db= -23
Ont[51]= 4256 ' db= -24
Ont[50]= 4105 ' db= -24
Ont[49]= 3960 ' db= -24
Ont[48]= 3820 ' db= -25
Ont[47]= 3685 ' db= -25
Ont[46]= 3555 ' db= -25
Ont[45]= 3429 ' db= -26
Ont[44]= 3308 ' db= -26
Ont[43]= 3191 ' db= -26
Ont[42]= 3079 ' db= -27
Ont[41]= 2970 ' db= -27
Ont[40]= 2865 ' db= -27
Ont[39]= 2764 ' db= -27
Ont[38]= 2666 ' db= -28
Ont[37]= 2572 ' db= -28
Ont[36]= 2481 ' db= -28
Ont[35]= 2393 ' db= -29
Ont[34]= 2309 ' db= -29
Ont[33]= 2227 ' db= -29
Ont[32]= 2148 ' db= -30
Ont[31]= 2072 ' db= -30
Ont[30]= 1999 ' db= -30
Ont[29]= 1929 ' db= -31
Ont[28]= 1860 ' db= -31
Ont[27]= 1795 ' db= -31
Ont[26]= 1731 ' db= -32
Ont[25]= 1670 ' db= -32
Ont[24]= 1611 ' db= -32
Ont[23]= 1554 ' db= -33
Ont[22]= 1499 ' db= -33
Ont[21]= 1446 ' db= -33
Ont[20]= 1395 ' db= -33
Ont[19]= 1346 ' db= -34
Ont[18]= 1298 ' db= -34
Ont[17]= 1252 ' db= -34
Ont[16]= 1208 ' db= -35
Ont[15]= 1165 ' db= -35
Ont[14]= 1124 ' db= -35
Ont[13]= 1085 ' db= -36
Ont[12]= 1046 ' db= -36
Ont[11]= 1009 ' db= -36
Ont[10]= 974 ' db= -37
Ont[9]= 939 ' db= -37
Ont[8]= 906 ' db= -37
Ont[7]= 874 ' db= -37
Ont[6]= 843 ' db= -38
Ont[5]= 813 ' db= -38
Ont[4]= 785 ' db= -38
Ont[3]= 757 ' db= -39
Ont[2]= 730 ' db= -39
Ont[1]= 704 ' db= -39
Ont[0]= 0 '679 ' db= -40
Return

PWM_Lookup_Table_60dB:
'HybrLo volume logscales 60dB - 13.10.2016
'for 16bit PWM values
Ont[127]= 65535 ' db= 0
Ont[126]= 62092 ' db= 0
Ont[125]= 58830 ' db= -1
Ont[124]= 55739 ' db= -1
Ont[123]= 52811 ' db= -2
Ont[122]= 50036 ' db= -2
Ont[121]= 47408 ' db= -3
Ont[120]= 44917 ' db= -3
Ont[119]= 42557 ' db= -4
Ont[118]= 40321 ' db= -4
Ont[117]= 38203 ' db= -5
Ont[116]= 36196 ' db= -5
Ont[115]= 34294 ' db= -6
Ont[114]= 32493 ' db= -6
Ont[113]= 30786 ' db= -7
Ont[112]= 29168 ' db= -7
Ont[111]= 27636 ' db= -8
Ont[110]= 26184 ' db= -8
Ont[109]= 24808 ' db= -8
Ont[108]= 23505 ' db= -9
Ont[107]= 22270 ' db= -9
Ont[106]= 21100 ' db= -10
Ont[105]= 19992 ' db= -10
Ont[104]= 18941 ' db= -11
Ont[103]= 17946 ' db= -11
Ont[102]= 17003 ' db= -12
Ont[101]= 16110 ' db= -12
Ont[100]= 15264 ' db= -13
Ont[99]= 14462 ' db= -13
Ont[98]= 13702 ' db= -14
Ont[97]= 12982 ' db= -14
Ont[96]= 12300 ' db= -15
Ont[95]= 11654 ' db= -15
Ont[94]= 11042 ' db= -15
Ont[93]= 10462 ' db= -16
Ont[92]= 9912 ' db= -16
Ont[91]= 9391 ' db= -17
Ont[90]= 8898 ' db= -17
Ont[89]= 8430 ' db= -18
Ont[88]= 7987 ' db= -18
Ont[87]= 7568 ' db= -19
Ont[86]= 7170 ' db= -19
Ont[85]= 6794 ' db= -20
Ont[84]= 6437 ' db= -20
Ont[83]= 6099 ' db= -21
Ont[82]= 5778 ' db= -21
Ont[81]= 5475 ' db= -22
Ont[80]= 5187 ' db= -22
Ont[79]= 4914 ' db= -23
Ont[78]= 4656 ' db= -23
Ont[77]= 4412 ' db= -23
Ont[76]= 4180 ' db= -24
Ont[75]= 3960 ' db= -24
Ont[74]= 3752 ' db= -25
Ont[73]= 3555 ' db= -25
Ont[72]= 3368 ' db= -26
Ont[71]= 3191 ' db= -26
Ont[70]= 3024 ' db= -27
Ont[69]= 2865 ' db= -27
Ont[68]= 2714 ' db= -28
Ont[67]= 2572 ' db= -28
Ont[66]= 2437 ' db= -29
Ont[65]= 2309 ' db= -29
Ont[64]= 2187 ' db= -30
Ont[63]= 2072 ' db= -30
Ont[62]= 1964 ' db= -30
Ont[61]= 1860 ' db= -31
Ont[60]= 1763 ' db= -31
Ont[59]= 1670 ' db= -32
Ont[58]= 1582 ' db= -32
Ont[57]= 1499 ' db= -33
Ont[56]= 1420 ' db= -33
Ont[55]= 1346 ' db= -34
Ont[54]= 1275 ' db= -34
Ont[53]= 1208 ' db= -35
Ont[52]= 1145 ' db= -35
Ont[51]= 1084 ' db= -36
Ont[50]= 1028 ' db= -36
Ont[49]= 974 ' db= -37
Ont[48]= 922 ' db= -37
Ont[47]= 874 ' db= -37
Ont[46]= 828 ' db= -38
Ont[45]= 785 ' db= -38
Ont[44]= 743 ' db= -39
Ont[43]= 704 ' db= -39
Ont[42]= 667 ' db= -40
Ont[41]= 632 ' db= -40
Ont[40]= 599 ' db= -41
Ont[39]= 568 ' db= -41
Ont[38]= 538 ' db= -42
Ont[37]= 509 ' db= -42
Ont[36]= 483 ' db= -43
Ont[35]= 457 ' db= -43
Ont[34]= 433 ' db= -44
Ont[33]= 411 ' db= -44
Ont[32]= 389 ' db= -45
Ont[31]= 369 ' db= -45
Ont[30]= 349 ' db= -45
Ont[29]= 331 ' db= -46
Ont[28]= 313 ' db= -46
Ont[27]= 297 ' db= -47
Ont[26]= 281 ' db= -47
Ont[25]= 267 ' db= -48
Ont[24]= 253 ' db= -48
Ont[23]= 239 ' db= -49
Ont[22]= 227 ' db= -49
Ont[21]= 215 ' db= -50
Ont[20]= 204 ' db= -50
Ont[19]= 193 ' db= -51
Ont[18]= 183 ' db= -51
Ont[17]= 173 ' db= -52
Ont[16]= 164 ' db= -52
Ont[15]= 155 ' db= -53
Ont[14]= 147 ' db= -53
Ont[13]= 140 ' db= -53
Ont[12]= 132 ' db= -54
Ont[11]= 125 ' db= -54
Ont[10]= 119 ' db= -55
Ont[9]= 112 ' db= -55
Ont[8]= 107 ' db= -56
Ont[7]= 101 ' db= -56
Ont[6]= 96 ' db= -57
Ont[5]= 91 ' db= -57
Ont[4]= 86 ' db= -58
Ont[3]= 81 ' db= -58
Ont[2]= 77 ' db= -59
Ont[1]= 69 ' db= -60
Ont[0]= 0 ' db= -96
Return

'[EOF]